## Slide 1: General Purpose Input/Output (GPIO)
Jalal Kawash

## Slide 2: Outline
The Raspberry Pi
Introduction to the RPi GPIO
Working with GPIO lines

## Slide 3: The Raspberry Pi
Section 1

## Slide 4: Section 1 Objective At the end of this section you will
Be familiar with the Raspberry Pi

## Slide 6
Image from raspberrypi.org

## Slide 7
From element14.com

## Slide 8: Raspberry Pi 2

## Slide 9: Technical Specs
900 MHz ARMv7 Quad Core Processor (Cortex-A7)
1GB RAM
40 pin extended GPIO
4 x USB 2 ports
CSI camera port (Raspberry Pi camera)
DSI display port (Raspberry Pi touch screen)
From element14.com

## Slide 10: Introduction to the Raspberry Pi GPIO
Section 2

## Slide 11: Section 2 Objectives At the end of this section you will
Get a quick look at the RPi GPIO pins
Look at example uses of the GPIO

## Slide 12: GPIO
General Purpose Input/Output device
Famous with microcontrollers
  Provide extended functions without changing circuitry
Has 54 lines
  Only a subset is available for the RPi
    26 lines in Pi1
    40 lines in Pi2

## Slide 13: RPi GPIO
Programmable
40 header pins on the RPi
Provide UART and 5V power
Provide others too e.g. CSI (camera serial interface) and DSI (Display serial interface)
Not plug and play

## Slide 14
www.ebay.com

## Slide 16
ebay.com

## Slide 17: Example Uses
Image from: www.raspberrypi.org

## Slide 18: Example Uses
Images from: learn.adafruit.com & kiwi.psnc.pl

## Slide 19: Example Uses
Image from: learn.adafruit.com

## Slide 20: Example Uses

## Slide 21: Example Uses

## Slide 22: Working with GPIO Lines
Section 3

## Slide 23: Section 3 Objectives At the end of this section you will
Have a closer look at GPIO registers
Know how to set functions to GPIO pins
Know how to use the pins for input and output

## Slide 24: RPi GPIO pins
The RPi GPIO has 16 GP pins
  Green ones
Since they are not plug-and-play, some work is need to initialize, write, and read
Each of these pins can have up to 6 functions
  For example function 1 is write & 0 is read
    From core’s point of view

## Slide 25: Pseudo Memory Mapped Registers
A memory-mapped register is dealt with as a memory address
  It is accessed by LDR & STR
A pseudo memory-mapped register is an actual peripheral register that is accessed as a memory location
  MMU deals with these requests
  MMU sends the request to the device rather than memory

## Slide 26: Pseudo Memory Mapped Registers
LDR r0, =0x3F200000
LDR r1, [r0]
Program
Address 0x3F200000 is a peripheral register
MMU
Register 0x3F200000
LDR
LDR
RAM
Regular Loads
GPIO registers are
pseudo
memory-mapped

## Slide 27: GPIO Registers
More info refer to: BCM2835 ARM Peripherals (available on BB)
Function
Select
Set
(Write 1)
Clear
(Write 0)
Level
(Read)

## Slide 28: GPIO Registers
There are more registers
Refer to: BCM2835 ARM Peripherals (available on BB) for more info
This document lists virtual addresses (in Linux) for registers
Replace 7E in the virtual address by 3F to obtain the physical address

## Slide 29: Function Select Registers
GPFSEL0
0x3F200000
For pins 0 to 9
GPFSEL1
0x3F200004
For pins 10 to 19
GPFSEL2
0x3F200008
For pins 20 to 29
GPFSEL3
0x3F20000c
For pins 30 to 39
GPFSEL4
0x3F200010
For pins 40 to 49
GPFSEL5
0x3F200014
For pins 50 to 53
Base GPIO address

## Slide 30: Accessing GPIO Registers
GPIO uses “pseudo” memory-mapped I/O
  Accessed as if accessing memory locations
unsigned int *gpio = 0x3F200000;
#define GPFSEL0 0
…
unsigned int v;
…
v = gpio[GPFSEL0];
gpio[GPFEL0] = v;

## Slide 31: Pin Offset from GPIO Base Address
A register corresponds to many GPIO pins
For example
Each pin (0 to 9) is controlled by 3 bits in GPFSEL0
For example, bits 0-2 set the function for GPIO pin 0
Each pin can be given a function (from up to 6 functions)
In our case, it is mostly input or output functions
GPFSEL0
For pins 0 to 9

## Slide 32: Inside GPFSEL0
From: BCM2835 ARM Peripherals

## Slide 33: Calculating the Pin Offset
If pin# is single-digit
  Offset = address for GPFSEL0 (base GPIO address, 0x3F200000)
If pin# > 9 (more than one digit)
  Offset = base GPIO address + 4*(pin# div 10)
  Address of GPFSEL1 to GPFSEL5
Example (pins 10 to 19):
  Offset = 0x3F200000 + 4*(1) = 0x3F200004
  Which is address for GPFSEL1

## Slide 34: Getting to Appropriate Pins
Given some pin#
Let GPFSEL{n} be the register that controls this pin#
  n = pin# div 10
Let d be the least significant digit of pin#
The 3 bits of GPFSEL{n} that select pin#’s function start at d*3
0-2
3-5
6-8
9-11
12-14
15-17
18-20
21-23
24-26
27-29
30-31
reserved
GPIOFSEL{n}
Pin
{n}0
Pin
{n}1
Pin
{n}2
Pin
{n}3
Pin
{n}4
Pin
{n}5
Pin
{n}6
Pin
{n}7
Pin
{n}8
Pin
{n}9

## Slide 35: GPFSEL registers
0
1
2
pin 0
3
4
5
pin 1
6
7
8
pin 2
9
10
11
pin 3
12
13
14
pin 4
15
16
17
pin 5
18
19
20
pin 6
21
22
23
pin 7
24
25
26
pin 8
27
28
29
pin 9
30
31
rsrvd
GPFSEL0
0
1
2
pin 10
3
4
5
pin 11
6
7
8
pin 12
9
10
11
pin 13
12
13
14
pin 14
15
16
17
pin 15
18
19
20
pin 16
21
22
23
pin 17
24
25
26
pin 18
27
28
29
pin 19
30
31
rsrvd
GPFSEL1
0
1
2
pin n0
3
4
5
pin n1
6
7
8
pin n2
9
10
11
pin n3
12
13
14
pin n4
15
16
17
pin n5
18
19
20
pin n6
21
22
23
pin n7
24
25
26
pin n8
27
28
29
pin n9
30
31
rsrvd
GPFSELn (n  {0 .. 5})

## Slide 36: Example
Pin 32
Register GPFSEL3, offset 0x3F20000c
  = 4*(32 div 10) + 0x3F200000
Least significant bit of pin# is 2
The three bits of GPFSEL3 that control pin 32 start at bit 3*2 = 6
Hence, bits 6-8 define the function of pin 32

## Slide 37: Setting the bits in GPFSEL{n}
Clear the appropriate bits in GPFSEL{n}
Set the appropriate bits in GPSFEL{n}

## Slide 38: Resetting the bits for pin 3
Reset GPFSEL0[9..11] to 000
AND GPFSEL0 with 1..1 000 111 111 111
~(7<<(((p)%10)*3))
b0111 << (3%10)* 3
b0111 << 9
shift left 9 bits
0..0 111 000 000 000
~(0..0 111 000 000 000)
1..1 000 111 111 111

## Slide 39: Resetting the bits for pin 3
#define GPIO_BASE 0x3F200000 // Address for GPIOFSEL0
unsigned *gpio = (unsigned*)GPIO_BASE; // GPIO base
*(gpio+((p)/10)) &= ~(7<<(((p)%10)*3))
Bitwise AND [0x3F200000] with 1..1 000 111 111 111
Pin 3 is an input pin now

## Slide 40: Clearing pin 3 bits (Input pin)
1
1
1
0..0
7<<9=
0
0
0
0
0
0
0
0
0
0
0
0
0..0
7=
0
0
0
0
0
0
1
1
1
?
?
?
?..?
GPFSEL0=
?
?
?
?
?
?
?
?
?
pin 0
pin 1
pin 2
pin 3
?
?
?
?..?
GPFSEL0=
?
?
?
?
?
?
?
?
?
pin 0
pin 1
pin 2
pin 3
0
0
0
1..1
~(7<<9)=
1
1
1
1
1
1
1
1
1
&
(AND)
0
0
0
?..?
GPFSEL0=
?
?
?
?
?
?
?
?
?
pin 0
pin 1
pin 2
pin 3
0
0
0
1..1
~(7<<9)=
1
1
1
1
1
1
1
1
1

## Slide 41: Resetting the bits for pin p
#define GPIO_BASE 0x3F200000 // Address for GPIOFSEL0
unsigned *gpio = (unsigned*)GPIO_BASE; // GPIO base
#define INP_GPIO(p) *(gpio+((p)/10)) &= ~(7<<(((p)%10)*3))

## Slide 42: Setting the bits for pin 3
Reset pin 3 (INP_GPIO(3))
*(gpio+((3)/10)) |= (1<<(((3)%10)*3))
(1<<(((3)%10)*3))
(1<<9)
0..0 001 000 000 000
Bitwise OR [0x3F200000] with 0..0 001 000 000 000
Pin 3 is an output pin now

## Slide 43: Example – Setting pin 3 bits
1
0
0
0..0
1<<9=
0
0
0
0
0
0
0
0
0
0
0
0
0..0
1=
0
0
0
0
0
0
0
0
1
0
0
0
?..?
?
?
?
?
?
?
?
?
?
pin 0
pin 1
pin 2
pin 3
1
0
0
0..0
0
0
0
0
0
0
0
0
0
|
OR
1
0
0
?..?
GPFSEL0=
?
?
?
?
?
?
?
?
?
pin 0
pin 1
pin 2
pin 3
0
0
0
?..?
GPFSEL0=
?
?
?
?
?
?
?
?
?
pin 0
pin 1
pin 2
pin 3

## Slide 44: Setting the bits for pin p
#define GPIO_BASE 0x3F200000 // Address for GPIOFSEL0
unsigned *gpio = (unsigned*)GPIO_BASE; // GPIO base
#define OUT_GPIO(p) *(gpio+((p)/10)) |= (1<<(((p)%10)*3))

## Slide 45: Reading and Writing Pins

## Slide 46: Performing I/O
Once a pin function is set, then pin can be used for I/O
To write to a pin, use GPSET{0,1} or GPCLR{0,1}
To read from a pin, use GPLEV{0,1}

## Slide 47
From: BCM2835 ARM Peripherals
Dividing a pin# by 32 determines which register must be used

## Slide 48: GPSET0 register
0
1
2
3
4
5
31
…
GPSET0
0
1
2
3
4
5
31
…
GPSET0
pin 0
pin 1
pin 2
pin 5
pin 31

## Slide 49: GPSET1 register
0
1
2
3
4
5
31
…
GPSET1
0
1
2
3
4
5
21
…
GPSET1
pin 32
pin 33
pin 34
pin 37
pin 53
reserved
Not used on the Pi

## Slide 50: GPSET0 Address
Base GPIO Address : 0x3F200000
GPSET0 : Base + 28 = 0x3F20001C
  28 decimal is 0x1C

## Slide 51: Setting (writing 1 to) a pin
0
0
0
…
0
1
2
0
3
0
31
GPSET0
0
0
0
…
0
1
2
1
3
0
31
GPSET0
Write 1 to pin 3
No effect on pin 2

## Slide 52: Setting (Writing to) a Pin
If writing 1, then use GPSET{n}, n= 0,1
  gpioAddr + 28 + {4*n}
    28 and 4*n are decimal values
If writing 0, use GPCLR{n}
  A write of 0 to GPSET{n} is ignored
  gpioAddr + 40 + {4*n}
    40 and 4*n are decimal values

## Slide 53: GPCLR0 register
0
1
2
3
4
5
31
…
GPCLR0
0
1
2
3
4
5
31
…
GPCLR0
pin 0
pin 1
pin 2
pin 5
pin 31

## Slide 54: Clearing (writing 0 to) a pin
0
0
0
…
0
1
2
0
3
0
31
GPCLR0
0
0
0
…
0
1
2
1
3
0
31
GPCLR0
Write 0 to pin 3
No effect on pin 2

## Slide 55: Example
To write 1 to (set) pin 3:
GPSET[3] = 1
To write 0 to (clear) pin 3:
GPCLR[3] = 1
GPSET[i] = 0 and GPCLR[i] =0 have no effect on pin

## Slide 56: Writing to pins 0 – 31
unsigned int *gpio = 0x3F200000;
#define GPSET0 7 \\ 28/4
#define GPCLR0 10 \\ 40/4
...
if (writing 1)
gpio[GPSET0] = 1 << pinNumber;
else
gpio[GPCLR0] = 1 << pinNumber;

## Slide 57: GPCLR1
Used to clear the remaining pins
Pins 32 to 53
Bit 0 clears pin 32, …
Not used on the Pi

## Slide 58
From: BCM2835 ARM Peripherals
X
Clear

## Slide 59: GPCLR0 Address
Base GPIO Address : 0x3F200000
GPCLR0 : Base + 40 = 0x3F200028

## Slide 60: Reading a Pin
Register GPLEVn is used to read a bit from a pin
In the RPi, only GPLEV0 is used
  Bit n corresponds to the value of pin n
Address of GPLEV0 is ox3F200000 + 52
  0x3F200034

## Slide 61: Inside GPLEV{n}
From: BCM2835 ARM Peripherals

## Slide 62: GPLEV0 register
0
1
2
3
4
5
31
…
GPLEV0
0
1
2
3
4
5
31
…
GPLEV0
pin 0
pin 1
pin 2
pin 5
pin 31

## Slide 63: GPLEVn Addresses
Base GPIO Address : 0x3F200000
GPLEV0 : Base + 52 = 0x3F200034
GPLEV1 : Base + 60 = 0x3F20003C
  Not used in the Pi

## Slide 64: Reading from pins 0 – 31
unsigned int *gpio = 0x3F200000;
#define GPLEV0 13
...
int v;
v = (gpio[GPLEV0] >> 3) & 1;
// v = pin 3 value

## Slide 65: Other GPIO functions
Clock signal
UART
JTAG
Etc …

## Slide 66: JTAG Interface
Joint Test Action Group
  IEEE 1149.1 Standard Test Access Port and Boundary-Scan Architecture
Originally used for IC debug ports
Embedded system development relies on JTAG to perform debugging
ARM11 has an extensive JTAG capability
EnableJTAG routine in jtag.s (by Dmitry Zavyalov)

## Slide 67: JTAG Interface Pins
www.raspberrypi-spy.co.uk

## Slide 68
ebay.com