## Slide 1: Digital Logic I. Basics
Jalal Kawash

## Slide 2: Outline
Introduction
  Binary Logic
  Logic Gates
  Boolean Functions & Logic Circuits
  Logic Circuits
Minterms and Gate-Level Minimization
  Minterms
  Boolean Sum of Products
  K-Maps
Digital Logic I
Basics

## Slide 3: Introduction
Section 1
Digital Logic I
Basics

## Slide 4: Section 1 Objectives At the end of this section you will
Recall binary logic and logic operators
Recall the definition of AND, OR, NOT, and XOR
See the correspondence between gates and logic operators
Build Boolean functions
Build digital logic circuits that correspond to Boolean functions
Digital Logic I
Basics

## Slide 5: Binary Logic
Deals with:
Binary variables
    Take values from {0, 1}
Logic operators
    Three basic operators: AND, OR, and NOT

## Slide 6: Logic Operators: AND
Switch x
Switch y
Output
x AND y

## Slide 7: Logic Operators: AND
Let x and y be binary variables, x.y or xy is defined by:
x | y | xy
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 8: Logic Operators: OR
Switch x
Output
Switch y
x OR y

## Slide 9: Logic Operators: OR
Let x and y be binary variables, x+y is defined by:
x | y | x+y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 10: Logic Operators: NOT
Let x be binary variables, x’ is defined by:
x | x’
0 | 1
1 | 0

## Slide 11: Precedence
Logic operators are applied in the following order:
Parentheses
NOT
AND
OR
Exercise: Create truth tables for x+xy’ and x+(xy)’

## Slide 12: Useful Logic Laws
x+0 = x | x.1 = x
x+x’ = 1 | x.x’ = 0
x+x = x | x.x = x
x+1 = 1 | x.0 = 0
(x’)’ = x | 
x+y = y+x | x.y = y.x
x + (y+z) = (x+y) + z | x(y.z) = (x.y)z
x(y + z) = x.y + x.z | x + y.z = (x+y)(x+z)
(x+y)’ = x’.y’ | (xy)’ = x’ + y’
x + xy = x | x(x+y) = x

## Slide 13: Useful Logic laws
Exercise: Verify these laws using truth tables

## Slide 14: Logic Gates
A logic gate is an electronic circuit that operates on one or more input signals to produce one output signal
Signals represent 0s and 1s
  Typically 0-1V for 0 and 2-3V for 1
Logic gates are basic building blocks for digital machines
There is a gate for each logic operator

## Slide 15: AND gate
x
y
xy
x | y | xy
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Think of it as a function :
bit and( bit x, bit y)

## Slide 16: OR gate
x
y
x+y
x | y | x+y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Think of it as a function :
bit or( bit x, bit y)

## Slide 17: NOT gate (invertor)
x
x’
x | x’
0 | 1
1 | 0
Think of it as a function :
bit not( bit x)

## Slide 18: More Gates: Exclusive OR (XOR)
x | y | xy
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x  y
x
y

## Slide 19: XOR is redundant
xy = x’y + y’x
xy = (x+y)(xy)’
Exercise: Verify these laws using truth tables

## Slide 20: More Gates: NOT OR (NOR)
x | y | x+y | (x+y)’
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
x
y
(x+y)’

## Slide 21: More Gates: NOT AND (NAND)
x | y | xy | (xy)’
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
x
y
(xy)’

## Slide 22: Gates with more inputs
It is possible to feed a gate (except invertors) more than 2 inputs
Note that this is equivalent to

## Slide 23: Boolean Functions
A Boolean function combines binary variables using logic operators.
Examples:
F1 = x + y’z
F2 = x’y’z + x’yz +xy’
  Exercise: Simplify to get x’z + xy’

## Slide 24: Boolean Function Exercises
Simplify:
xyz’ +x’yz+xyz+x’yz’
  Answer: y
(x+y’+z’)(x’+z’)
  Answer: z’ +x’y’
yz(xz+x’+xz’)
  Answer: yz

## Slide 25: Logic Circuits
A logic circuit is formed of logic gates and calculates a Boolean function
Example: x’y +y’x
Source: DL1.circ (xor1)

## Slide 26: Logisim
Free simulator for logic circuits
Downloadable from various places
  http://sourceforge.net/projects/circuit/
Demo!
  XOR1 & XOR2

## Slide 27: Another XOR Circuit
xy = (x+y)(xy)’
Source: DL1.circ (xor2)

## Slide 28: Boolean Function Exercises
Draw the corresponding logic circuit:
xyz’ +x’yz+xyz+x’yz’
  Answer: y
(x+y’+z’)(x’+z’)
  Answer: z’ +x’y’
yz(xz+x’+xz’)
  Answer: yz

## Slide 29: F = z’ +x’y’
Source: DL1.circ (Example1 Function)
  F = z’ +x’y’
x’
y’
z’
x’y’

## Slide 30: Boolean Function Exercise
What is the Boolean function corresponding to the following circuit?
Source: DL1.circ

## Slide 31: Self-Test Quiz
What is the Boolean functions corresponding to the following circuit?
F1
F2

## Slide 32: Minerms and Gate-Level Minimization
Digital Logic I
Basics
Section 2

## Slide 33: Section 2 Objectives At the end of this section you will
Master the Boolean-Sum-of-Products algorithm
Convert truth tables to Boolean functions
Minimize minterms in a function using factorization
Minimize minterms in a function in canonical form using K-Maps
Digital Logic I
Basics

## Slide 34: Boolean Sum of Products (BSP)
Truth table = Boolean function(s) = Logic Circuit
BSP Algorithm:
  Given a truth table, convert each column C to an equivalent function FC as follows:
  For each output column, for each row R where the output is 1:
    fR = empty
    For each input value x in R that is 1, fR = fR.x
    For each input value x in R that is 0, fR = fR.x’
  FC = R fR

## Slide 35: BSP Example
x | y | xy
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x’y
xy’
F = x’y + xy’ = x y

## Slide 36: BSP Example
Convert the following table to 2 functions F1 and F2
What do F1 and F2 represent?
x | y | z | F1 | F2
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 37: Minterms
BSP is often called sum of minterms
Example: minterms with three variables
Minterm symbol | Minterm | Corrsponding binary number
mo | x’y’z’ | 000
m1 | x’y’z | 001
m2 | x’yz’ | 010
m3 | x’yz | 011
m4 | xy’z’ | 100
m5 | xy’z | 101
m6 | xyz’ | 110
m7 | xyz | 111

## Slide 38: Understanding minterms
mi corresponds to the binary number i
(Assume a 3-variable function)
If i = 1, i in binary is 001
m1 is x’y’z
  That is, if the digit is 0, negate the corresponding variable (x’ and y’)
  If the digit is 1, leave the corresponding variable as is (z)

## Slide 39: Minterms Canonical Form
A function is in canonical form if it is a sum of minterms
Examples:
F1(x, y, z) = x’yz’ + x’yz + xy’z
  F1(x, y, z) = m2 + m3 + m5
  F1(x, y, z) =  (2, 3, 5)
F2(x, y, z) = x’y’z’ + x’y’z + x’yz’ + x’yz
  F2(x, y, z) = m0 + m1 + m2 + m3
  F2(x, y, z) =  (0, 1, 2, 3)

## Slide 40: Karnaugh-Maps
A K-map is a visual representation of a Boolean function in canonical form
It helps in the process of simplifying a function
An n-variable function in canonical form will have up to 2n minterms
The form in which the variable appear in a term (such as x or x’) is called a literal
In an n-variable function, each minterm consists of n literals (e.g. x’yz’ in a 3-variable function)

## Slide 41: 2-Variable Functions
Minterms:
mo | x’y’ | 00
m1 | x’y | 01
m2 | xy’ | 10
m3 | xy | 11
2-variable map:
m0
m1
m2
m3

## Slide 42: 2-Variable Maps
F1 = x’y’ + x’y + xy is
m0
m1
m2
m3
F2 = x’y’ + xy’ is
m0
m1
m2
m3

## Slide 43: Adjacency
Two squares in a map are said to be adjacent if the corresponding minterms differ in one literal only.
Example m0 and m1 are adjacent
  m0 = x’y’ and m1 is x’y
  Differ in y
  Similarly, m0 and m2 are adjacent
  m2 and m3
  m1 and m3
m0
m1
m2
m3

## Slide 44: Simplifying Functions
Two adjacent squares can be combined to eliminate the different literal
Example: x’y + xy = y(x+x’) = y(1) = y
A map gives us clues as to which minterms should be combined

## Slide 45: Example
F (x, y) =  (1, 2, 3)
Combine 1 and 3
Combine 2 and 3
F = x’y + xy’ + xy
F = x’y + xy + xy’ + xy (since xy + xy = xy)
F = y(x’+x) + x (y’+y)
F = y + x
m0
m1
m2
m3

## Slide 46: 2-Variable Map Observations
The number of adjacent squares that can be combined is a power of 2
A single square represents a minterm with 2 literals (e.g. x’y)
2 adjacent squares represent one minterm with 1 literal (e.g. x)
4 adjacent squares represent the function F = 1

## Slide 47: 3-Variable Functions
mo | x’y’z’
m1 | x’y’z
m2 | x’yz’
m3 | x’yz
m4 | xy’z’
m5 | xy’z
m6 | xyz’
m7 | xyz
m0
m1
m4
m5
m3
m2
m7
m6

## Slide 48: Adjacency
Same definition
m0
m1
m4
m5
m3
m2
m7
m6
Adjacent too

## Slide 49: Adjacency
0 and 2 are adjacent
  000 and 010: they differ in one bit
  The corresponding minterms x’y’z’ and x’yz’ only differ in y
Note that 1 and 2 are not adjacent
  001 and 010: they differ in more than one bit
  Hence, the first row of the map is drawn as 0, 1, 3, 2 instead of 0, 1, 2, 3

## Slide 50: Example
F(x, y, z) =  (2, 3, 4, 5)
m0
m1
m4
m5
m3
m2
m7
m6
To simplify, combine
  3 and 2
  4 and 5

## Slide 51: Example
F(x, y, z) =  (2, 3, 4, 5)
F = x’yz’ + x’yz + xy’z’ + xy’z
F = x’y (z’+z) + xy’(z’+z)
F = x’y + xy’
F = x  y
m0
m1
m4
m5
m3
m2
m7
m6

## Slide 52: Example
F(x, y, z) =  (3, 4, 6, 7)
F = x’yz + xy’z’ + xyz’ + xyz
Combine
  4 and 6
  7 and 6
F = x’yz + xy’z’ + xyz’ + xyz + xyz’
F = x’yz + xz’ + xy
m0
m1
m4
m5
m3
m2
m7
m6

## Slide 53: Example
Also combine
  3 and 7
F = x’yz + xz’ + xy
F = xz’ + xy + x’yz + xyz
F = xz’ + xy + yz
m0
m1
m4
m5
m3
m2
m7
m6

## Slide 54: 3-Variable Map Observations
A single square represents 1 minterm with three literals (e.g., x’yz’)
2 adjacent squares represent one minterm with 2 literals (e.g., xy’)
4 adjacent squares represent one minterm with 1 literal (e.g., z)
8 adjacent squares represent the function F = 1

## Slide 55: Example
F = x’y’z’ + x’y’z + x’yz + x’yz’
Combine (0,1), (1,3), (3,2), (2,0)
F = x’
One literal
m0
m1
m4
m5
m3
m2
m7
m6

## Slide 56: 4-Vraiable Maps
m0
m1
m4
m5
m3
m2
m7
m6
m12
m13
m8
m9
m15
m14
m11
m10

## Slide 57: Adjacency
m0
m1
m4
m5
m3
m2
m7
m6
m12
m13
m8
m9
m15
m14
m11
m10

## Slide 58: 4-Variable Map Observations
A single square represents 1 minterm with 4 literals (e.g., wx’yz’)
2 adjacent squares represent one minterm with 3 literals (e.g., xy’z)
4 adjacent squares represent one minterm with 2 literal (e.g., w’z)
8 adjacent squares represent one minterm with 1 literal (e.g., z’)
16 adjacent squares is the function F = 1

## Slide 59: Self-Test Quiz
Draw a 4-variable K-map and simplify the following functions:
F(w, x, y, z) =  (0, 1, 5, 8, 9)
F(w, x, y, z) =  (1, 3, 5, 6, 9, 10, 11, 15)

## Slide 60: Higher-Order K-Maps
A 5-variable map is 3-D
More dimensions are needed for higher order maps
Useful only with computer programs

## Slide 61: Optional Topics
Maxterms
Boolean product of sums (product of maxterms)
5-variable and 6-variable maps