## Slide 1: Digital Logic II. Combinational Circuits
Jalal Kawash

## Slide 2: Outline
Types of Circuits
Basic Combinational Circuits
  Adders
  Decodres
ALUs
More Combinational Circuits
  Multiplexers
  Multipliers
  Comparators
Digital Logic II
Combinational Circuits

## Slide 3: Types of Digital Circuits
Digital Logic 2
Combinational Circuits
Section 1

## Slide 4: Section 1 Objective At the end of this section you will
Understand the difference between combinational and sequential circuits
Digital Logic II
Combinational Circuits

## Slide 5: Combinational Circuits
A combinational circuit is a logic circuit whose output is solely determined by the inputs
Combinational Circuit
…
n
inputs
…
m
outputs

## Slide 6: Sequential Circuits
Unlike a combinational circuit, the output of a sequential circuit at time t can affect the circuits output at time t+1

## Slide 7: Sequential Circuits
Combinational Circuit
inputs
outputs
Memory

## Slide 8: Basic Circuits
Digital Logic II
Combinational Circuits
Section 2

## Slide 9: Section 2 Objectives At the end of this section you will
Be able to build half-adder (HA) circuits
Understand HA limitations
Be able to build full-adder (FA) circuits
Chain combinational circuits
Be able to build decoders
Understand how to use decoders as “switches” to build mult-function circuits
Digital Logic II
Combinational Circuits

## Slide 10: Half Adder (HA)
Input: two bits, x and y
Output: x + y
x | y | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 11: HA Circuit
Sum = x’y + y’x = x  y
Carry = xy
x | y | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Source: DL2.circ (HA)
Sum
Carry

## Slide 12: Limitation of a HA
Can we build an adder for 2-bit numbers from the 1-bit HAs?
2-bit Adder
x
y
xo
x1
y1
y0
x+y
carry

## Slide 13: Limitation of a HA
Can we build an adder for 2-bit numbers from the 1-bit HAs? Does not work if x0 + y0 produce a carry!
x =
x1
x0
y =
y1
y0
+
Can use a HA to produce
sum and possibly a carry
What if there is anon-zero carry?
1
Need an adder with 3 inputs
HA has only 2!

## Slide 14: Full Adder (FA)
Input: three bits, x, y, and z
Output: x + y + z
x | y | z | Sum | Carry
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 15: Full Adder – BSP for Carry
x | y | z | Sum | Carry
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
x’yz
xy’z
xyz’
xyz

## Slide 16: Carry Function
Carry = x’yz + xy’z + xyz’ + xyz
Carry = x(y’z +yz’) + yz
Carry = x(yz) + yz
m0
m1
m4
m5
m3
m2
m7
m6

## Slide 17: Full Adder – BSP for Sum
x | y | z | Sum | Carry
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
x’y’z
x’yz’
xy’z’
xyz

## Slide 18: Sum Function
Sum = x’y’z + x’yz’ + xy’z’ + xyz
Map is useless!!
m0
m1
m4
m5
m3
m2
m7
m6

## Slide 19: Sum Function
Observation: (a  b)’ = a’b’ + ab
Proof:
  (a  b)’ = (a’b + b’a)’ xor definition
  (a  b)’ = (a’b)’(b’a)’ DeMorgan’s law
  (a  b)’ = (a’’ + b’)(b’’ + a’) DeMorgna’s law
  (a  b)’ = (a + b’)(b + a’) Double negation
  (a  b)’ = ab + a’a + b’b + a’b’ Distribution
  (a  b)’ = ab + a’b’ xx’ = 0, x+0=x

## Slide 20: Sum Function
Sum = x’y’z + x’yz’ + xy’z’ + xyz
Sum = x’(y’z + yz’) + x(y’z’ + yz)
Sum = x’(y  z) + x(y  z)’
Sum = x  y  z
  Let a = (y  z), Sum = x’a + xa’ = x  a

## Slide 21: FA Circuit
Sum = x  y  z
Carry = x(yz) + yz
Source: DL2.circ (FA)
Carry out
Sum

## Slide 22: Chaining FAs (2-bit number FA)
FA
x
y
z
S
C
Add x1x0 to y1y0
FA
x0
y0
0
S0
Co
FA
x1
y1
S1
C1o
Result is C1S1S0

## Slide 23: 4-bit Adder
FA
x0
y0
0
S0
FA
x1
y1
S1
FA
x2
y3
S2
FA
x3
y3
S3
C1o

## Slide 24: Chaining
Chaining is an easy way to build “higher-order” circuits from “lower-order” ones
However, it is not the best
The longer the chain the slower the circuit
s0
time
s1
s2

## Slide 25: Full Subtractor
Can be built from a FA
x – y = x (y  1) + 1
Why?

## Slide 26: Decoders
A decoder is a combinational circuit such that
  It has n inputs
  It has 2n outputs
  For each input a unique associated output line carries 1
  All other lines carry 0
  Let bn be the binary number corresponding to the input bits
  If the input is bn, then line bn is set (carries 1)

## Slide 27: 2-4 Decoder
2-4 Decoder
I0
I1
F0
F1
F2
F3
2-4 Decoder
0
0
F0
F1
F2
F3

## Slide 28: 2-4 Decoder
2-4 Decoder
0
1
F0
F1
F2
F3
2-4 Decoder
1
0
F0
F1
F2
F3

## Slide 29: 2-4 Decoder
2-4 Decoder
1
1
F0
F1
F2
F3

## Slide 30: Multi-Function Circuits
Hardware runs all the time
A multi-function circuit will compute all of its functions
A decoder is used to “filter out” the functions that are not required

## Slide 31: 4-Function Circuit
F0
F1
F2
F3
2-4 Decoder
I0
I1
F0
F1
F2
F3
Data
input
Selected
Function

## Slide 32: 2-4 Decoder (Truth Table)
x | y | F0 | F1 | F2 | F3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1

## Slide 33: 2-4 Decoder (Circuit)
Source: DL2 (2-4 Decoder)

## Slide 34: 3-8 Decoder
Exercise

## Slide 35: A Simple ALU
Section 3
Digital Logic II
Combinational Circuits

## Slide 36: Section 3 Objectives At the end of this section you will
Build a simple 1-bit ALU
Use chaining to build higher order ALU
Digital Logic II
Combinational Circuits

## Slide 37: Bit Slice
A bit slice is a 1-bit ALU
We will use chaining to create a larger ALU
ALU can do
  And
  Or
  Not
  Addition
  Only

## Slide 38: Logic Unit
xy
x+y
y’
Source: DL2 (Logic Unit)

## Slide 39
x
y
I0
I1
Full Adder
Decoder
Logic Unit
OR
xy
x+y
y’
Sum(x,y)
Carry
Output  {xy, x+y, y’ , Sum(x,y)}
Carry out
Carry
in
Bit slice

## Slide 40
Bit slice demo
Source: DL2.circ (Bit Slice)

## Slide 41: 4-bit ALU (by chaining)
Source: DL2 (4-bit ALUS)

## Slide 42: More Combinational Circuits
Section 4
Digital Logic II
Combinational Circuits

## Slide 43: Section 4 Objective At the end of this section you will
Gain more practice with combinational circuits
Digital Logic II
Combinational Circuits

## Slide 44: Multiplexers
If S = 0, X = I0
If S = 1, X = I1
Multiplexer
I0
I1
S
X  {I0, I1}

## Slide 45: 4-Input Multiplexer
Source: D2l.circ (4-input Multiplexer)
S1
S0
I0
I1
I2
I3

## Slide 46: Shifters
A 1-bit left/right shifter.
C = 0 for left 1 for right
1-bit left/right shifter.
C = 0 for left 1 for right

## Slide 47: Left Shift
C = 0
D0D1D2D3D4D5D6D7
D1D2D3D4D5D6D7 0
D1
D2
D3
D4
D5
D6
D7
D1
D2
D3
D4
D5
D6
D7
0
0
0
0
0
0
0
0

## Slide 48: Right Shift
C = 1
D0D1D2D3D4D5D6D7
0 D0D1D2D3D4D5D6
D1
D2
D3
D4
D5
D6
0
D0
D1
D2
D3
D4
D5
D6
0
0
0
0
0
0
D0
0
From Tanenbaum, Structured Computer Organization, Fifth Edition, (c) 2006 Pearson Education, Inc. All rights reserved.

## Slide 49: Comparators
Two bits can be compared with a XOR gate
Two numbers can be compared bit-wise

## Slide 50: Magnitude Comparator
Challenge yourself with designing a circuit that inputs 2-bit binary numbers A & B
It has 3 outputs:
  First output is 1, iff the numbers are equal
  Second is 1, iff A < B
  Third is 1, iff A > B
Repeat for 4 bit numbers

## Slide 51: Multipliers
Multiplication can be done by addition
To multiply X and Y, add Y to itself X times; or add X to itself Y times
Challenge yourself to build a “direct” multiplier
  i.e., do not use the method described above
  Hint: fix the size of your inputs; e.g., multiply 2-bit by a 3-bit number

## Slide 52: Self-Test Quiz
Challenge yourself to build a “direct” multiplier that multiplies 2-bit by a 3-bit number