## Slide 1: Digital Logic III. Sequential Circuits
Jalal Kawash

## Slide 2: Outline
Introduction
  Types of Sequential Circuits
  Clocks
Basic Memory Circuits
  Latches
  Flip-Flops
Synchronous Sequential Circuits
  Finite State Machines
Digital Logic III
Sequential Circuits

## Slide 3: Introduction
Section 1
Digital Logic III
Sequential Circuits

## Slide 4: Section 1 Objectives At the end of this section you will
Understand the two types of sequential circuits
Understand clock signals
Digital Logic III
Sequential Circuits

## Slide 5: Combinational Circuits
A combinational circuit is a logic circuit whose output is solely determined by the inputs
Combinational Circuit
…
n
inputs
…
m
outputs

## Slide 6: Sequential Circuits
Unlike a combinational circuit, the output of a sequential circuit at time t can affect the circuits output at time t+1

## Slide 7: Sequential Circuits
Combinational Circuit
inputs
outputs
Memory

## Slide 8: Types of Sequential Circuits
Synchronous: Employ clock signals
  Clock signals affect memory at discrete time
  Also called “clocked”
Asynchronous: Do not employ clocks
  Rely on signal propagation delay to affect memory
  Harder to design
In the course, I will only talk about synchronous circuits

## Slide 9: Synchronous Sequential Circuits
Combinational Circuit
inputs
outputs
Memory
Clock

## Slide 10: Clocks
A clock is a device that pulses at regular intervals
Synchronous sequential Circuits can be:
  level-triggered: Memory is activated during a level
    E.g: during the high level
here
  edge-triggered: Memory is activated when signal changes
    E.g: from 0 to 1 (positive edge) or 1 to 0 (negative edge)
    Used more

## Slide 11: Basic Memory Circuits
Digital Logic III
Sequential Circuits
Section 2

## Slide 12: Section 2 Objectives At the end of this section you will
Build 1-bit memory circuits
Understand latches
Realize problems with latches
Build flip-flops from latches
Construct higher-capacity registers from flip-flops
Digital Logic III
Sequential Circuits

## Slide 13: Basic Memory Circuits
Latches
Digital Logic III
Sequential Circuits
Section 2

## Slide 14: Latches
A latch is a level-triggered, single-bit memory
The Set-Rest (SR) latch:
R
S
Q
Q’

## Slide 15: NOR Truth Table
x | y | x+y | (x+y)’
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0

## Slide 16: Setting the latch, S = 1, R = 0 (memory = Q = 1)
1
0
0
0
1
R
S
Q
Q’

## Slide 17: Resetting the latch, S = 0, R = 1 (memory = Q = 0)
1
0
0
0
1
R
S
Q
Q’

## Slide 18: S = R = 0?
0
0
Behaviour depends on previous state, Q
R
S
Q
Q’

## Slide 19: When Q = 1
0
0
1
0
1
0
No Change
R
S
Q
Q’

## Slide 20: When Q = 0
0
0
0
1
0
1
No Change
R
S
Q
Q’

## Slide 21: S = R = 1?
1
1
Contradicts requirement that Q and Q’ are opposites
0
0
Prohibited
R
S
Q
Q’

## Slide 22: Clocked SR
Q
Q’
Source: DL3.circ (Clocked-SR)
Demo

## Slide 23: Clocked SR
This is a positive-level triggered latch
When Clock is 0, R & S have no effect

## Slide 24: D-Latch
There is no S=R=1 state
Q
Q’
D-latch demo
Source: DL3.circ (D-latch)

## Slide 25: SR Latch with NAND Gates
Source: DL3.circ (NAND SR-Latch)

## Slide 26: SR-Latch Comparison
NOR
NAND
R=S=0 has no effect
R=S=1 prohibited
R=S=1 has no effect
R=S=0 prohibited

## Slide 27: Problem With Latches
Latches are level-triggered, so circuits can become unreliable

## Slide 28: Why unreliable?
D latch
D
clock
Q
clock
1
1
0
1
1
1
0
0
0
0
?

## Slide 29: Basic Memory Circuits
Flip-Flops
Digital Logic III
Sequential Circuits
Section 2

## Slide 30: Flip-Flops
Flip-flops are also 1-bit memory circuits
They are edge triggered
They solve the unreliability issue with sequential circuits that employ latches
Flip-flops are the basis for registers

## Slide 31: D Flip-Flop (Master-Slave)
D-Latch 2
Source: DL3.circ (D Flip Flop, D-Latch 2

## Slide 32: D Flip-Flop (Master-Slave)
1
0
V
V
V
Slave latch is not affected
Q does not change
Clk
Clk
D
D

## Slide 33: D Flip-Flop (Master-Slave)
0
1
V
Master latch is not affected
Q changes to V
V
V
This is a negative-edge triggered flip-flop
Clk
Clk
D
D
No change

## Slide 34: Symbols for D-Flip-Flops
D
D
Positive-edge
Negative-edge

## Slide 35: 8-bit Register
Works as a signal amplifier
Octal flip-flop

## Slide 36: Memory Organization
Logic diagram for a
4 x 3 memory.
Each row is one of the four 3-bit words.
Chip select
Read (1) – Write (0)
Output Enabled
Decoder

## Slide 37: Writing
Logic diagram for a
4 x 3 memory.
Each row is one of the four 3-bit words.
0
1

## Slide 38: Reading
Logic diagram for a
4 x 3 memory.
Each row is one of the four 3-bit words.
1
1
1
From Tanenbaum, Structured Computer Organization, Fifth Edition, (c) 2006 Pearson Education, Inc. All rights reserved.

## Slide 39: Finite State Machines
Digital Logic III
Sequential Circuits
Section 2

## Slide 40: Section 3 Objective At the end of this section you will
Design sequential circuits as Finite State Machines
Digital Logic III
Sequential Circuits

## Slide 41: Finite State Machines
Hardware is typically designed as an FSM
An FSM is equivalent to an synchronous DL circuit
FSM
  A finite set of states
  A set of transitions
Example: A simple Air-conditioning system

## Slide 42: Simple Air-Conditioning System
Can be only controlled by a remote device
  Device has two buttons: POWER and SPEED
AC has two fan speeds: LOW and HIGH
When turned on it always starts in LOW
POWER switches it ON and OFF
SPEED toggles between both speeds
  When on LOW, goes to HIGH
  When on HIGH goes to LOW

## Slide 43: FSM
HIGH
LOW
OFF
POWER
POWER
POWER
SPEED
SPEED
SPEED

## Slide 44
POWER | SPEED | Current State | Next State
1
OFF
LOW
1
LOW
OFF
1
HIGH
OFF
0
OFF
OFF
0
LOW
HIGH
0
HIGH
LOW
HIGH
LOW
OFF
POWER
POWER
POWER
SPEED
SPEED
SPEED
0
0
0
1
1
1

## Slide 45
POWER | SPEED | Current State | Next State
1 | 0 | OFF | LOW
1 | 0 | LOW | OFF
1 | 0 | HIGH | OFF
0 | 1 | OFF | OFF
0 | 1 | LOW | HIGH
0 | 1 | HIGH | LOW
0 | 0 | OFF | OFF
0 | 0 | LOW | LOW
0 | 0 | HIGH | HIGH

## Slide 46
POWER | SPEED | Current State | Next State
1 | 0 | OFF | LOW
1 | 0 | LOW | OFF
1 | 0 | HIGH | OFF
0 | 1 | OFF | OFF
0 | 1 | LOW | HIGH
0 | 1 | HIGH | LOW
0 | 0 | OFF | OFF
0 | 0 | LOW | LOW
0 | 0 | HIGH | HIGH
Replace:
OFF by 00
LOW by 01
HIGH by 10

## Slide 47
POWER | SPEED | Current State | Next State
1 | 0 | 00 | LOW
1 | 0 | LOW | 00
1 | 0 | HIGH | 00
0 | 1 | 00 | 00
0 | 1 | LOW | HIGH
0 | 1 | HIGH | LOW
0 | 0 | 00 | 00
0 | 0 | LOW | LOW
0 | 0 | HIGH | HIGH
Replace:
OFF by 00
LOW by 01
HIGH by 10

## Slide 48
Replace:
OFF by 00
LOW by 01
HIGH by 10
POWER | SPEED | Current State | Next State
1 | 0 | 00 | LOW
1 | 0 | LOW | 00
1 | 0 | HIGH | 00
0 | 1 | 00 | 00
0 | 1 | LOW | HIGH
0 | 1 | HIGH | LOW
0 | 0 | 00 | 00
0 | 0 | LOW | LOW
0 | 0 | HIGH | HIGH

## Slide 49
Replace:
OFF by 00
LOW by 01
HIGH by 10
POWER | SPEED | Current State | Next State
1 | 0 | 00 | 01
1 | 0 | 01 | 00
1 | 0 | HIGH | 00
0 | 1 | 00 | 00
0 | 1 | 01 | HIGH
0 | 1 | HIGH | 01
0 | 0 | 00 | 00
0 | 0 | 01 | 01
0 | 0 | HIGH | HIGH

## Slide 50
Replace:
OFF by 00
LOW by 01
HIGH by 10
POWER | SPEED | Current State | Next State
1 | 0 | 00 | 01
1 | 0 | 01 | 00
1 | 0 | HIGH | 00
0 | 1 | 00 | 00
0 | 1 | 01 | HIGH
0 | 1 | HIGH | 01
0 | 0 | 00 | 00
0 | 0 | 01 | 01
0 | 0 | HIGH | HIGH

## Slide 51
Replace:
OFF by 00
LOW by 01
HIGH by 10
POWER | SPEED | Current State | Next State
1 | 0 | 00 | 01
1 | 0 | 01 | 00
1 | 0 | 10 | 00
0 | 1 | 00 | 00
0 | 1 | 01 | 10
0 | 1 | 10 | 01
0 | 0 | 00 | 00
0 | 0 | 01 | 01
0 | 0 | 10 | 10

## Slide 52
Three inputs: two bits (P&S) from the device
And two (B&C) bits representing the state the FSM is in
Two output bits (XY) determining the next state
P | S | AB | XY
1 | 0 | 00 | 01
1 | 0 | 01 | 00
1 | 0 | 10 | 00
0 | 1 | 00 | 00
0 | 1 | 01 | 10
0 | 1 | 10 | 01
0 | 0 | 00 | 00
0 | 0 | 01 | 01
0 | 0 | 10 | 10

## Slide 53: Boolean Sum of Products for X
X = P’SA’B + P’S’AB’
= P’(SA’B + S’AB’)
P | S | AB | XY
1 | 0 | 00 | 01
1 | 0 | 01 | 00
1 | 0 | 10 | 00
0 | 1 | 00 | 00
0 | 1 | 01 | 10
0 | 1 | 10 | 01
0 | 0 | 00 | 00
0 | 0 | 01 | 01
0 | 0 | 10 | 10

## Slide 54: Boolean Sum of Products for Y
Y = PS’A’B’ + P’SAB’ + P’S’A’B
=S’A’ (PB’ + P’B) + P’SAB’
=S’A’ (P  B) + P’SAB’
P | S | AB | XY
1 | 0 | 00 | 01
1 | 0 | 01 | 00
1 | 0 | 10 | 00
0 | 1 | 00 | 00
0 | 1 | 01 | 10
0 | 1 | 10 | 01
0 | 0 | 00 | 00
0 | 0 | 01 | 01
0 | 0 | 10 | 10

## Slide 55: The Combinational Circuit
Source:DL3.circ (AC Combinational)

## Slide 56: A Sequential Circuit?
Not yet
The FSM needs to ‘remember’ current state to be used to determine next state
Store X and feed it back to B
Store Y and feed it back to C

## Slide 57: The Sequential Circuit
Source: LD3.circ (AC Sequential)
AC
Comb

## Slide 58: The System
Source: LD3.circ (AC System)
AC Sequential
Demo
x
y
xy
xy’
F1
F2
F3
F4
x | y | F1 | F2 | F3 | F4
0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1 | 1
Low Speed
High Speed
F1 = F2 = xy
F3 = F4 = xy’

## Slide 59: Timer Example
10
01
00
TICK
TICK
TICK

## Slide 60
10
01
00
TICK
TICK
TICK
A | B | Tick | Anew | Bnew
0 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
Anew = A’BT + AB’T
Bnew = A’B’T + A’BT’
= A’(BT)

## Slide 61
Source: LD3.circ (Timer)
Demo