## Slide 1: Microarchitecture Design & Operation
Suggested Reading: Chapter 4 from Tanenbaum, Structured Computer Organization, 5/6ed, Pearson

## Slide 2: Layered Computer Organization
Device Level
Digital Logic Level
Microarchitecure Level
OS Level
Problem-Oriented Language Level
Assembly Language Level
Instruction Set Architecture Level

## Slide 3: Instruction set architecture
IJVM

## Slide 4: Objectives
By the end of this section, you will be able to:
List and work with the IJVM ISA instructions
Translate a subset of Java programs to IJVM ISA
Understand stack machines

## Slide 5: JVM
javac: Java compiler
  Compiles HL Java to Bytecode
  Bytecode = Java Assembly (JAS) Language
JVM: Java Virtual Machine
  Invoked by the java command
  An interpreter of Java Bytecode

## Slide 6: Java Architecture
void xyz() {
  i = j + k;
  if (i == 3)
  …
}
Hardware
Java code
javac
.java file
.class file
java

## Slide 7: Example .java code

## Slide 8: Example .class file

## Slide 9: IJVM
IJVM: subset of JVM that deals with integers
  No floating point instructions
All integer JAS opcodes are 1-byte long
  Simpler to deal with

## Slide 10: Stacks
JVM is a stack machine
Stacks are used to push local procedure variables
  Local variable frame: data structure between LV and SP

## Slide 11: Local Variable Frame
Use of a stack for storing local variables.
While A is active.
After A calls B.
After B calls C.
After C and B return and A calls D.

## Slide 12: Operand Stacks
JVM is an operand stack machine
Stacks are used to push operands during the computation of arithmetic expressions

## Slide 13: Operand Stack
Use of an operand stack for doing an arithmetic computation
(a1 = a2+a3)
SP

## Slide 14: The IJVM Memory Model
The various parts of the IJVM memory.

## Slide 15: Constant Pool
Constants, strings, & pointers to other areas of memory
Does not change after loading (cannot be written by IJVM program)
CPP contains the address of the first word

## Slide 16: Local Variable Frame / Operand Stack
allocated to variables stored for the lifetime of a procedure
at the beginning of the frame: parameters
then, local variables
then operand stack
  not true in general
LV points to the start of LVF
TOS = word at top of stack

## Slide 17: Method Area
Program text
PC points to the instruction to be fetched next

## Slide 18: Offsets
CPP, LV, & SP : word pointers
  Offset is a word
  LV+1: second word in LFV
  SP: word on top of stack, SP – 1, next to top word
PC: byte address
  Offset is a byte
  PC+1: next byte is to be fetched

## Slide 19: The IJVM Instruction Set
The IJVM instruction set. The operands byte, const, and varnum
are 1 byte. The operands disp, index, and offset are 2 bytes.

## Slide 21: Compiling Java to IJVM
A Java fragment.
The corresponding Java assembly language.
The IJVM program in hexadecimal.

## Slide 22: Stack When Executing Bytecode
The stack after each instruction of Fig. 4-14(b).

## Slide 23: IVOKEVIRTUAL disp
Invokes another method
disp (16 bit) = position in constant pool that contains the address in method area where method starts
disp
CP
address
MA
Method
invoked

## Slide 24: IVOKEVIRTUAL disp
SIMPLIFIED: cannot call methods except in same object
  No Object-Orientation!
Caller:
  Pushes OBJREF being called onto stack
    Not needed for IJVM
  Pushes method parameters
    First parameter is param 1

## Slide 25: IVOKEVIRTUAL disp
First 4 bytes of a method
  First 2: number of parameters, including OBJREF (param 0)
  Second 2: size of local variable area
disp
CP
address
MA
2
3
1
0
Byte[0] Byte[1] = unsigned 16 bit int
Byte[2] Byte[3] = unsigned 16 bit int
OPCODE1

## Slide 26: INVOKEVIRTUAL
Memory before executing INVOKEVIRTUAL.
After executing it.
LV = SP - # of params
Params + local vars
PC = first Opcode in method area (5th byte)

## Slide 27: IRETURN
Memory before executing IRETURN.
After executing it.
Restore LV and PC to old values
Control is returned to opcode immediately after INVOKEVIRTUAL

## Slide 28: Exercise
Convert the following HL Java code to IJVM
int j = 100
int s = 0
for (int i = 0; i < j; i++)
s += i

## Slide 29
.main // main program
.var // local variables for main
  i
  j
  s
.end-var

## Slide 30
start:
BIPUSH 0x64 // 100
ISTORE j
BIPUSH 0x0
DUP
ISTORE s
ISTORE i

## Slide 31
check:
ILOAD i
ILOAD j
ISUB // i - j
IFLT for_body // i < j
GOTO end
for_body:
// s += i
ILOAD i
ILOAD s
IADD
ISTORE s

## Slide 32
// i++
ILOAD i
BIPUSH 0x1
IADD
ISTORE i
GOTO check
end:
.end-main

## Slide 33: Input and Output Author: Dan Stone
.main
L1: IN // request character input from memory
DUP // duplicate top of stack (input char) for comparing
BIPUSH 0x0 // push 0x0 for comparison
IF_ICMPEQ L2 // if no characters are available for input, loop
OUT // else, print character
GOTO L1 // loop back to beginning of program
L2: POP // No key has been pushed, so clear the stack,
GOTO L1 // and start over
.end-main

## Slide 34: Defining Methods in JAS typically after main
.method methodName()
.var
variables
.end-var
body
…
IRETURN
.end-method

## Slide 35: Calling Methods in JAS
LDC_W OBJREF
INVOKEVIRTUAL methodName
Before .main, you need:
.constant
  OBJREF 0x40
.end-constant

## Slide 36: Calling Methods with Parameters
LDC_W OBJREF
ILOAD param1
ILOAD param2
INVOKEVIRTUAL methodName

## Slide 37: Using LDC_W
// this program displays all the printable ASCII values 32..126
.constant
  one 1
  start 32
  stop 126
.end-constant
.main
LDC_W start
  next: DUP
  OUT // output the current character
  DUP
  LDC_W stop
  ISUB IFEQ done // exit if we've reached the end
  LDC_W one
  IADD
  GOTO next // increment and do the next one done
  POP
  HALT
.end-main

## Slide 38: Exercise
Write a JAS method int sum(int n) that calculates and returns the sum of integers up to n,

## Slide 39: HL Java code (static method)

## Slide 40: JAS code
Using Jclasslib byte code viewer
iconst loads a constant to the stack
sum is var 1
i is var 2
Parameter n is var 0

## Slide 41: HL Java code (instance method)

## Slide 42: JAS code
Variables are shifted by 1, since var 0 is OBJREF
Static
Instance