## Slide 1: Microarchitecture Design & Operation
Suggested Reading: Chapter 4 from Tanenbaum, Structured Computer Organization, 5/6ed, Pearson

## Slide 2: The Data path
IJVM

## Slide 3: Objectives
At the end of this section, you will be able to
Understand the data path of a hypothetical architecture
Understand data-path timing
Understand how the data path is controlled

## Slide 4: Contemporary Multilevel Machines
A six-level computer.
The support method for each level is indicated below it .

## Slide 5: Example: IJVM
Integer JVM
  Subset of JVM
Will design hardware to interpret IJVM byte code (Java assembly language)
Microprogram (in ROM)
  Fetch-decode-execute IJVM instructions
  interpreter

## Slide 6: Interpreter (1)
An interpreter for a simple computer (written in Java).
. . .

## Slide 7: Interpreter (2)
An interpreter for a simple computer (written in Java).

## Slide 8: IJVM Data Path
32–bit registers (except MBR: 8-bit register)
Registers accessible only by the microprogram
Correspond to a variable with a similar name in ISA
Registers drive their contents onto the B-Bus to the ALU
ALU output drives the shifter and then the C-Bus
C-Bus can write any register(s)

## Slide 9: ALU
Except: 32-bit ALU

## Slide 10: ALU Controls
6 controls:
  F0 & F1 : ALU function
  ENA
  ENB
  INVA
  INC : add 1 to the result

## Slide 11: ALU Signal Combinations
Useful combinations of ALU signals and the function performed.

## Slide 12: AND Function (00)
Useful combinations of ALU signals and the function performed.

## Slide 13: OR Function (01)
Useful combinations of ALU signals and the function performed.

## Slide 14: NOT Function (10)
Useful combinations of ALU signals and the function performed.

## Slide 15: Adder Function (11)
Useful combinations of ALU signals and the function performed.

## Slide 16: ALU Inputs
B can be loaded from ONE of 8 registers, in 9 ways
Loaded from H only:
H can be loaded from any of the registers feeding the B-bus, unchanged through the ALU

## Slide 17: Shifter
2 controls:
  SLL8 : shift left logical 1 byte, 8 least significant bits are zeroed
  SRA1 : shift right arithmetic by 1 bit leaving the most significant bit unchanged

## Slide 18: Data Path Timing
It is possible to read and write the same register in one cycle
Example: increment SP
Put SP on B-bus
Pass it through the ALU with no left input and INC asserted
Store it in SP
This is possible due to data path timing

## Slide 19: Data Path Timing
Timing diagram of one data path cycle.
ALU/Shifter runs all the time
No clock pulse that triggers it to run
Output is garbage before
w + x + y from the cycle start time

## Slide 20: Registers
Memory Address Register
Memory Data Register
Program Counter
Memory Byte Register
Stack Pointer
Local Variables
Constant Pool Pointer
Top Of Stack
Old Program Counter
High order ALU input

## Slide 21: Control Signals
Enable Register’s output onto B
Enable Register’s Input from C

## Slide 22: Memory Operation
Communicate with memory via 2 ports
8-bit:byte-addressable controlled by PC
32-bit: word-addressable controlled by MAR and MDR
PC = address of byte which when read goes to MBR
MAR = address of word (32-bits) which when read goes to MDR
MAR = address of word (32-bits) which when written comes from MDR

## Slide 23: Memory Operation
MAR contains word addresses
PC contains byte addresses
PC = 2, third byte in memory (byte 2)
  Starting a memory read, brings byte 2 to MBR
MAR = 2, third word in memory (bytes 8-11)
  Starting a memory read brings 4 bytes to MDR
PC/MBR: read ISA-level instructions (byte code)
MAR/MDR: read ISA-level data

## Slide 24: Word Addressing
Actual physical implementation: memory is byte addressable
MAR is wired into address bus as follows:
Two logical left shifts: multiply by 4
When MAR is 1, address 4 is put on the address bus (word 1 starts at byte 4)
High order bits are discarded: only 4-GB memory is allowed

## Slide 25: Byte Addressing
MBR can be copied onto bus B in two ways
  Unsigned or signed
Unsigned: (0)24MBR is put on B
  Useful when assembling 16 bit integer
Signed value [-128, 127]
(MBR[7])24MBR is put on B (Sign extension)

## Slide 26: Data Path Cycle
Gating registers out on B
ALU and shifter operation
Driving the output on C
Storing C into one or more registers
In addition:
Memory operations, if any, start at the end of the cycle

## Slide 27: Memory Operation Timing
Registers are loaded at the rising edge of the clock
Start memory
operation
somewhere here
Memory is working
Input to MDR/MBR
Is ready
MDR/MBR loaded
here
Data brought
From memory
Available now
ASSUMES memory takes one cycle: not true in reality, but simplifies design
MDR/MBR can be
used while
another mem read
is in progress

## Slide 28: Control Signals
Enable Register’s output onto B
Enable Register’s Input from C
Control the ALU and Shifter
Memory Control Signals

## Slide 29: Controlling the Data Path
Need 29 signals:
9 to enable register output on B
8 to control ALU and shifter
9 to enable register input from C
2 to indicate memory read/write via MAR/MDR
1 to indicate memory fetch via PC/MBR
4
24

## Slide 30: Controlling the Data Path
So, we need 24 bits to control the DP for one cycle (one microinstruction)
Ignore for now
36 bit microinstruction

## Slide 31: Microinstructions

## Slide 32: 4-16 Decoder
4-16 decoder

## Slide 33: 4-16 Decoder
4-16 decoder
0
0
0
0

## Slide 34: 4-16 Decoder
4-16 decoder
0
0
0
1

## Slide 35: 4-16 Decoder
4-16 decoder
0
1
0
1

## Slide 36: Mic-1

## Slide 37: Sequencer
Mic-1 is given an ISA instruction
Sequencer produce
  State of every control signal
  Next (address) microinstruction to be executed

## Slide 38: Mic-1

## Slide 39: Mic-1
Think of it as memory holding the microprogram
contains 512 36-bit microinstructions
Unlike main memory, microprogram need not be stored sequentially (very messy)
Instead of incrementing micro program counter, each microinstruction specifies its successor

## Slide 40: Next Microinstruction

## Slide 41: Mic-1

## Slide 42: Mic-1

## Slide 43: Mic-1

## Slide 44: Notes
MPC = microprogram counter; points to next microinstruction (MI)
The instruction pointed to by MPC is loaded to MIR (MicroInstruction Register)
  MIR = ControlStore[MPC]
A single MI sets up the signals for DP and memory
First 4 bytes (B) drive a decoder to select exactly one register to be gated on bus B
  Gating more than one register gives an unreliable value and can damage hardware
The memory (M) 3 bits send commands to memory ports: read, write, or fetch
  Read=1: MDR = Memory[MAR]
  Write=1: Memory[MAR] = MDR
  Fetch=1: MBR = Memory[PC]

## Slide 45: Notes
The 9 C bits enable as many registers as need to be written at the end of a DP cycle
The 8 ALU bits drive the ALU (6 bits) and the shifter (2 bits)

## Slide 46: Mic-1

## Slide 47: Data Path Timing
Timing diagram of one data path cycle.
Load
MIR
MIR =
CS[MPC]
N & Z

## Slide 48: Mic-1
w
x
y
z

## Slide 49: Next Microinstruction
JAM: three Jumping bits

## Slide 50: Next MI
(JAMZ AND Z) OR
(JAMN AND N) OR
NEXT_ADRRESS[8]
Either:
NEXT_ADDRESS does not change, or
NEXT_ADDRESS[8] is set to 1

## Slide 51: Next Microinstruction
A microinstruction with JAMZ set to 1 has two potential successors.
Next if Z flip-flop = 0
Next if Z flip-flop = 1
JAMZ

## Slide 52: Mic-1
If JMPC == 1
MBR OR (bw) NEXT_ADDRESS[0..7]
Else
Pass NEXT_ADDRESS as is from previous MI

## Slide 53: JMPC & MBR
When JMPC == 1, NEXT_ADDRESS[0..7] is typically 0’s
NEXT_ADDRESS[8] = 0 or 1
MBR has a fetched opcode from main memory
Oring Next_ADDRESS[0..7] with MBR gives a unique address in the micro store
This address is the first microinstruction where interpretation of the opcode starts
1
1
Or
0
0
0
0
0
0
0
0

## Slide 54: MBR

## Slide 55: Data Path Timing
Timing diagram of one data path cycle.
Load
MIR
MIR =
CS[MPC]
N & Z
Including MDR and MBR, if at all, from cycle 0
Need MBR, N, and Z

## Slide 56: Mic-1

## Slide 57: CPU Clock Speed
The time it takes for DP cycle (microinstruction execution) defines the CPU clock speed
For example, a 3.0 GHz CPU can execute 3 billion microinstructions per second
  Or, 3 microinstructions in a nanosecond