## Slide 1: Microarchitecture Design & Operation
Suggested Reading: Chapter 4 from Tanenbaum, Structured Computer Organization, 5/6ed, Pearson

## Slide 2: The microprogram
IJVM

## Slide 3: Objective
At the end of this module you will be able to
Understand, develop, and extend the Mic-1 microprogram

## Slide 4
microprogram

## Slide 5: Invariants
The following are always maintained
SP points at the top of the stack, before and after each ISA instruction
TOS always contains the value at the top of the stack, before and after each ISA instruction
Each MI always fetches the opcode for the following MI in the program

## Slide 6: Implementation of IJVM Using the Mic-1 (1)
The microprogram for the Mic-1

## Slide 7: Implementation of IJVM Using the Mic-1 (2)
The microprogram for the Mic-1

## Slide 8: Implementation of IJVM Using the Mic-1 (3)
The microprogram for the Mic-1

## Slide 9: Implementation of IJVM Using the Mic-1 (4)
The microprogram for the Mic-1

## Slide 10: Implementation of IJVM Using the Mic-1 (5)
The microprogram for the Mic-1

## Slide 11: Microinstructions
Best way to specify microinstructions is to give the 36 bit stream
However, this is tough
We will give a HL notation
  Better for us to understand

## Slide 12: Notation
Each line: activities in a single clock cycle
SP = SP + 1; rd
  Read SP onto B-Bus
  ALU: add 1 operation
  Store back in SP
  Initiate a memory read instruction
    MDR = Memory[MAR]

## Slide 13: Notation
SP = MDR = SP +1
  B = SP
  ALU + 1
  Store result in SP and MDR
MDR = SP; wr
  Copy SP into MDR
  Start a memory write
    Memory[MAR] = MDR

## Slide 14: Invalid Instructions
MDR = SP + MDR
Cannot be executed in one cycle
Need 2 cycles:
  H = MDR (alternatively H = SP)
  MDR = SP + H

## Slide 15: Invalid Instructions
H = H – MDR
  Why illegal?
ALU functions

## Slide 16: Invalid Instructions
MAR = SP; rd
MDR = H
Illegal:
  rd => MDR = Memory[MAR]
  Completes at the end of second microinstruction
  Second microinstruction also assigns value to MDR
  Result: unknown value in MDR
Microassembler must reject such statements

## Slide 17: Permitted Microinstructions
All permitted operations.
SOURCE in {MDR, PC, MBR, MBRU, SP, LV, CPP, TOS, OPC} (to B bus)
DEST in {MAR, MDR, PC, SP, LV, CPP, TOS, OPC, H} (from C bus)
Also rd, wr, fetch
Any of the
above operations may be extended
by adding ‘‘<< 8’’ to them to shift the
result left by 1 byte. For example,
a common operation is
H = MBR << 8

## Slide 18: Interpreter
An interpreter for a simple computer (written in Java).

## Slide 19: Interpretation
main1 PC = PC + 1; fetch; goto(MBR)
0’s
0001
MPC = NEXT_ADDRESS OR MBR = MBR

## Slide 20: Microstore
Address | Microinstruction
… | 
0x10 | Start of microcode to interpret BIPUSH
… | 
0x57 | Start of microcode to interpret POP
0x58 | ?
0x59 | Start of microcode to interpret DUP
POP needs three microinstructions
Cannot be fit contiguously in microstore
Every MI must point to its successor

## Slide 21: NEXT_ADDRESS
Address | Microinstruction
… | 
0x57 | First microcode to interpret POP
… | 
? | Second microcode to interpret POP
… | 
? | Third microcode to interpret POP
… | 
Main1 | PC = PC+1; fetch; goto(MBR)
Last MI that interprets an ISA instruction has Main1 as its successor

## Slide 22: Interpretation
Main loop of the micro program
main1 PC = PC + 1; fetch; goto(MBR)
main1: label (address)
goto: unconditional branch
Assumes PC has been fetched previously and points to first byte in method area
Typically first byte in main method
PC is incremented and next byte is fetched
Next byte will be ready in MBR at the end of the next microinstruction
May be needed by the third microinstruction

## Slide 23: Interpretation
main1 PC = PC + 1; fetch; goto(MBR)
MBR = POP = 0x57
MPC = 0x57
For the next MI

## Slide 24: JMPC
If JMPC == 1
MBR OR (bitwize) NEXT_ADDRESS[0..7]
Else
Pass NEXT_ADDRESS as is from previous MI

## Slide 25: NOP
nop1 goto main1
Do nothing
First microinstruction to be executed
No Operation
main1

## Slide 26: IADD Pop 2 words from stack and add them; push result onto stack
x
y
S’
x+y
S’

## Slide 27: IADD – cycle 1 Pop 2 words from stack and add them; push result onto stack
x
y
S’
x
TOS
SP
Need to read y to DP
x
y
S’
SP
, MAR
Read: MDR = Memory[MAR] = y

## Slide 28: IADD – cycle 2 Pop 2 words from stack and add them; push result onto stack
x
TOS
Wait for the read to finish
y
S’
SP
, MAR
Mean while copy TOS to H to perform
A+B (TOS=x+MDR=y)
x
H
At the beginning of cycle 3, MDR = y

## Slide 29: IADD – cycle 3 Pop 2 words from stack and add them; push result onto stack
x
TOS
Add MDR and H (x+y)
y
S’
SP
, MAR
Need to write (x+y) back to memory:
MDR = (x+y) write
x
H
Also update TOS to (x+y), new top of stck
y
MDR
x+y
x+y
End of cycle 4
x+y

## Slide 30: IADD Pop 2 words from stack and add them; push result onto stack
iadd1 MAR = SP = SP – 1; rd; goto iadd2
iadd2 H = TOS; goto iadd3
iadd3 MDR = TOS= MDR+H; wr; goto main1
From now on implicit goto’s will be omitted
Note: iadd1 = 0x60

## Slide 31: IADD – iadd1
iadd1 MAR = SP = SP – 1; rd; goto iadd2
MIR
iadd2
SP
Pop 2 words from stack and add them; push result onto stack

## Slide 32: IADD – iadd2
iadd2 H = TOS; goto iadd3
MIR
iadd3
TOS

## Slide 33: IADD – iadd3
iadd3 MDR = TOS= MDR+H; wr; goto main1
MIR
main1
MDR

## Slide 34: ISUB
isub1 MAR = SP = SP – 1; rd;
isub2 H = TOS;
isub3 MDR = TOS= MDR – H ; wr; goto main1
Note: isub1 = 0x64
Pop 2 words from stack and subtract them; push result onto stack

## Slide 35: IAND
iand1 MAR = SP = SP – 1; rd;
iand2 H = TOS;
iand3 MDR = TOS= MDR AND H ; wr; goto main1
Note: iand1 = 0x7E
Pop 2 words from stack and and them; push result onto stack

## Slide 36: IOR
ior1 MAR = SP = SP – 1; rd;
ior2 H = TOS;
ior3 MDR = TOS= MDR OR H ; wr; goto main1
Note: ior1 = 0x80
Pop 2 words from stack and or them; push result onto stack

## Slide 37: DUP – cycle 1
Duplicate top word on stack and push onto stack
x
S’
SP
?
x
S’
SP
, MAR
x
TOS

## Slide 38: DUP – cycle 2
Duplicate top word on stack and push onto stack
x
S’
SP
?
x
S’
SP
, MAR
x
TOS
x
MDR
Write TOS to memory:
Copy TOS to MDR
Memory[MAR] = MDR = x
x

## Slide 39: DUP
dup1 MAR = SP = SP + 1;
dup2 MDR = TOS; wr; goto main1
Note: dup1 = 0x59
Duplicate top word on stack and push onto stack

## Slide 40: POP
pop1 MAR = SP = SP – 1; rd;
pop2
pop3 TOS= MDR; goto main1
Note: pop1 = 0x57
Delete word from stack

## Slide 41: POP – pop2
pop2
Simply: goto pop3
NEXT
ADDRESS
pop3
none

## Slide 42: SWAP
swap1 MAR = SP – 1; rd;
swap2 MAR = SP
swap3 H = MDR; wr
swap4 MDR = TOS
swap5 MAR = SP – 1; wr
swap6 TOS = H; goto main1
Note: swap1 = 0x5F
Swap top of stack word with next-to-top word

## Slide 43: Exercise
Write an implementation in MAL for a hypothetical IJVM instruction DNTT
  Duplicate Next To Top
  Duplicates the next-to-top value on the stack and push onto stack

## Slide 44: Instructions with Operands

## Slide 45: Fetching a head
…
1) IADD
2) DUP
3) ISUB
main1 PC = PC + 1; fetch; goto(MBR)
PC = 1, MBR = IADD
PC = 2, fetch DUP to MBR
Interpret IADD
End of add1: MBR = DUP
When IADD finishes, goto main1
PC = 3, fetch ISUB, goto dup1
End of dup1: MBR = ISUB

## Slide 46: BIPUSH byte
Push byte onto stack
BIPUSH 1
DUP
What does MBR contain?

## Slide 47: Mic-1
NOP

## Slide 48
nop1 goto main1
main1 PC = PC + 1; fetch; goto(MBR)
PC = 1, fetch the first opcode
MBR is still zero
MBR will contain the first opcode at the end of next cycle

## Slide 49: Mic-1
NOP

## Slide 50
nop1 goto main1
main1 PC = PC + 1; fetch; goto(MBR)
PC = 2, fetch the second byte (which is operand 1)
MBR = BIPUSH, at the end of nop1
MBR will contain the operand 1 at the end of next cycle
BIPUSH
1
DUP

## Slide 51: BIPUSH byte
bipush1 SP = MAR = SP + 1
(now MBR = 1)
bipush2 MDR = TOS = MBR; wr; goto main1
main1 PC = PC + 1; fetch; goto(MBR)
Need another cycle before MBR contains next byte (DUP) in the ISA program
Goto (MBR) will go to 1, which is not a lead MI!
First attempt
BIPUSH
1
DUP

## Slide 52: BIPUSH byte
bipush1 SP = MAR = SP + 1
bipush2 PC = PC + 1; fetch
bipush3 MDR = TOS = MBR; wr; goto main1
Note: bipush1 = 0x10
Push byte onto stack

## Slide 53: ILOAD varnum
Push local variable onto stack, varnum is one byte (except in the WIDE format)
Local variables and parameters are treated similarly
Variables are referenced by LV + varnum
varnum 0 is OBJREF, which we do not use

## Slide 54: ILOAD varnum
Push local variable onto stack, varnum is one byte (except in the WIDE format)
Old Stack
Link Pointer
LV
Value of varnum 1
Value of varnum 2
Caller’s PC
Caller’s LV
SP
?
Value of varnum

## Slide 55: ILOAD varnum
iload1 H = LV
iload2 MAR = MBRU + H; rd
iload3 MAR = SP = SP + 1
iload4 PC = PC + 1; fetch; wr
iload5 TOS = MDR; goto main1
Note: iload1 = 0x15
Push local variable onto stack, varnum is one byte (except in the WIDE format)

## Slide 56: ISTORE varnum
istore1 H = LV
istore2 MAR = MBRU + H
istore3 MDR = TOS; wr
istore4 SP = MAR = SP – 1; rd
istore5 PC = PC + 1; fetch
istore6 TOS = MDR; goto main1
Note: istore1 = 0x36
Pop word from stack and store it in a local variable

## Slide 57: IINC
The IINC instruction has two different operand fields.
Add const to local variable, both operands are 1 byte each

## Slide 58: IINC varnum const
iinc1 H = LV
iinc2 MAR = MBRU + H; rd
iinc3 PC = PC + 1; fetch
iinc4 H = MDR
iinc5 PC = PC + 1; fetch
iinc6 MDR = MBR + H; wr; goto main1
Note: iinc1 = 0x84
Add const to local variable, both operands are 1 byte each

## Slide 59: GOTO offset
goto1 OPC = PC – 1
goto2 PC = PC + 1; fetch
goto3 H = MBR << 8
goto4 H = MBRU OR H
goto5 PC = OPC + H; fetch
goto6 goto main1
Note: goto1 = 0xA7
OPC = address of the GOTO
MBR = 1st byte of offset; Fetch 2nd
Shift signed MBR Left 1 byte
H = 16 bit signed offset
Calculate absolute offset; fetch it for next MI
Unconditional branch, offset is 16-bit signed

## Slide 60: GOTO
The situation at the start of various microinstructions.
a) Main1. b) goto1. c) goto2. d) goto3. e) goto4.

## Slide 61: Conditional Branching
MPC[8] = (JAMZ AND Z) OR (JAMN AND N) OR NEXT_ADRRESS[8]
Either:
NEXT_ADDRESS does not change, or
NEXT_ADDRESS[8] is set to 1

## Slide 62: IFLT offset
iflt1 MAR = SP = SP – 1; rd
iflt2 OPC = TOS
iflt3 TOS = MDR
iflt4 N = OPC; if (N) goto T; else goto F
Note: iflt1 = 0x9B
Pop word from stack and branch to offset if < 0

## Slide 63: iflt1
iflt1 MAR = SP = SP – 1; rd
Read in next-to-top word from stack
NEXT
ADDRESS
iflt2
SP

## Slide 64: iflt2
iflt2 OPC = TOS
Save top of stack in OPC, before it is lost
NEXT
ADDRESS
iflt3
TOS

## Slide 65: iflt3
iflt3 TOS = MDR
MDR now has next-to-top word on stack; this is the new top of the stack
NEXT
ADDRESS
iflt4
MDR

## Slide 66: iflt4
iflt4 N = OPC; if (N) goto T; else goto F
Run OPC through ALU to see if it is 0 (OPC has old top of stack); branch on N
NEXT
ADDRESS
F
OPC

## Slide 67: Labels T and F
if (N) goto T; else goto F
MPC[8] = (JAMZ AND Z) OR (JAMN AND N) OR NEXT_ADRRESS[8]
If N = 1, MPC[8] = 1
Else MPC[8] = 0
MPC[0..7] does not change

## Slide 68: Labels T & F
if (N) goto T; else goto F
T & F must differ only in the high-order bit
For T it is 1 for F it is 0
Remaining bits are the same

## Slide 69: Branching to T
If N = 1
MIR
F
OPC
AND
N
flipflop
MPC
F
High Order Bit
MPC
F
1
MPC
T
=
OR

## Slide 70: Branching to F
If N = 0
MIR
F
OPC
AND
N
flipflop
MPC
F
High Order Bit
MPC
F
0
MPC
F
=
OR

## Slide 71: F
F PC = PC + 1; goto F2
F2 PC = PC + 1; fetch; goto F3
F3 goto main1
Skip second offset byte; goto F2
Fetch new opcode
No need to Branch

## Slide 72: T
T OPC = PC – 1; goto goto2
Same as goto (OPC = PC – 1 is goto1)
We could have said:
T goto goto1
But this wastes a cycle
Branch to offset

## Slide 73: GOTO
goto1 OPC = PC – 1
goto2 PC = PC + 1; fetch
goto3 H = MBR << 8
goto4 H = MBRU OR H
goto5 PC = OPC + H; fetch
goto6 goto main1

## Slide 74: IFEQ offset
ieq1 MAR = SP = SP – 1; rd
ieq2 OPC = TOS
ieq3 TOS = MDR
ieq4 Z = OPC; if (Z) goto T; else goto F
(same as IFLT, but Z is used instead of N)
Note: ifeq1 = 0x99
Pop word from stack and branch to offset if it is = 0

## Slide 75: IF_ICMPEQ offset
if_icmpeq1 MAR = SP = SP – 1; rd
if_icmpeq2 MAR = SP = SP – 1
if_icmpeq3 H = MDR; rd
if_icmpeq4 OPC = TOS
if_icmpeq5 TOS = MDR
if_icmpeq6 Z = OPC – H; if (Z) goto T; else goto F
Note: if_icmpeq1 = 0x9F
Pop 2 words from stack and branch to offset if equal

## Slide 76: WIDE
The BIPUSH instruction format.
ILOAD with a 1-byte index.
WIDE ILOAD with a 2-byte index.

## Slide 77: WIDE
The initial microinstruction
sequence for ILOAD
and WIDE ILOAD. The
addresses are examples.

## Slide 78: WIDE

## Slide 79: WIDE LOAD
Fetch first byte of operand
Goto wide_iload1
Fetch next opr byte

## Slide 80: WIDE STORE

## Slide 81: LDC_W

## Slide 82: Calling INVOKEVIRTUAL
LDC_W OBJREF
INVOKEVIRTUAL noParamMethod
.constant
OBJREF 0x40
.end-constant

## Slide 83: Calling INVOKEVIRTUAL
LDC_W OBJREF
ILOAD param
INVOKEVIRTUAL oneParamMethod
.constant
OBJREF 0x40
.end-constant

## Slide 84: IVOKEVIRTUAL disp
Invokes another method
disp (16 bit) = position in constant pool that contains the address in method area where method starts
disp
CP
address
MA
Method
invoked

## Slide 85: IVOKEVIRTUAL disp
First 4 bytes of a method
  First 2: number of parameters, including OBJREF (param 0)
  Second 2: size of local variable area
disp
CP
address
MA
2
3
1
0
Byte[0] Byte[1] = unsigned 16 bit int
Byte[2] Byte[3] = unsigned 16 bit int
OPCODE1

## Slide 86: INVOKEVIRTUAL

## Slide 87: INVOKEVIRTUAL disp

## Slide 88: IRETURN

## Slide 89: IRETURN

## Slide 90: Modifying the microprogram
MMV Example

## Slide 91: MMV File Types
JAS: source files containing IJVM ISA
  For example ex.jas on BB
IJVM: MMV assembles JAS files to IJVM files
MAL: the microprogram is stored in a MAL file (mic1ijvm.mal)
MIC1: MMV assembles MAL files to MIC1 files
Once JAS or MAL files are assembled, the corresponding IJVM or MIC1 files need only be loaded

## Slide 92: Adding MDUP
Add the instruction MDUP byte which works like DUP except that it is repeated byte times
For instance, MDUP 5 duplicates the top of the stack 5 times

## Slide 93: 1. Write your MAL code
mdup1 PC = PC + 1; fetch; // fetch next opcode
mdup2 OPC = MBR; // save operand
mdup3 N = OPC; if (N) goto myT1; else goto myF1 // if neg quit
mdup4 Z = OPC; if (Z) goto myT2; else goto myF2 // if zero quit
mdup5 SP = MAR = SP + 1 // one more word on the stack
mdup6 MDR = TOS; wr // write TOS to stack
mdup7 OPC = OPC -1; goto mdup4 // dec OPC and repeat
myT1 goto Main1 //quit
myT2 goto Main1 //quit
myF1 goto mdup4 //continue
myF2 goto mdup5 //continue

## Slide 94: 1. Write your MAL code
Do not skip line numbers
  Like mdup1, mdup3, without mdup2
No need for implicit goto
mdup1 PC = PC + 1; fetch; goto mdup2
mdup2 OPC = MBR;
Keep in mind that “True” and “False” labels must be 10000000 apart
  Microassembler takes care of this
  Use new labels
No need

## Slide 95: 2. Optimize your MAL code
mdup1 PC = PC + 1; fetch; // fetch next opcode
mdup2 OPC = MBR; // save operand
mdup3 N = OPC; if (N) goto myT1; else goto myF1 // if neg quit
mdup4 Z = OPC; if (Z) goto myT2; else goto myF2 // if zero quit
mdup5 SP = MAR = SP + 1 // one more word on the stack
mdup6 MDR = TOS; wr // write TOS to stack
mdup7 OPC = OPC -1; goto mdup4 // dec OPC and repeat
myT1 goto Main1 replace with PC = PC + 1; fetch; goto (MBR)
myT2 goto Main1 replace with PC = PC + 1; fetch; goto (MBR)
myF1 goto mdup4 replace with Z = OPC; if (Z) goto myT2; else goto myF2
myF2 goto mdup5 replace with SP = MAR = SP + 1 ; goto mdup6
myT1 goto Main1
myT2 goto Main1
myF1 goto mdup4

## Slide 96: 3. Add your code to mic1ijvm.mal
Code can be added after any instruction that ends with an explicit goto
MDUP now needs a numeric value for the opcode
Add it at the beginning of the file as
.label mdup1 0x01
Use any hex value that is not in use

## Slide 97: 3. Add your code to mic1ijvm.mal

## Slide 98: 4. Modify ijvm.conf
Add:
0x01 MDUP byte // duplicates the top of the stack byte times
Anywhere in the file

## Slide 99: 5. Assemble the Microcode
Run MMV from a directory that contains ijvm.conf
From MMV, load/Assemble MAL file
  Choose mic1ijvm.mal
[if there are errors MMV will tell you]
Load (effectively loading mic1ijvm.mic1)

## Slide 100: 5. Assemble the Microcode (NOTES)
You may get a Java.lang.NullPointerException or Java.lang.Exception when assembling some MAL code in MMV. Two things can help you recover from these, which I have learned the hard way: 1. Make sure there is an empty line at the end of you MAL file 2. If your code contains multi-way branching (if-else), add your code gradually to the MAL file as follows: (a) Add all microinstrcutions (MI) that precede the next MI that has if-else. (So this chunk you have just added does not have any if-else MIs). Compile this part alone and correct any errors before proceeding. (b) add the following if-else MI, compile, and correct errors.
GOTO (a) until all MIs have been added to the MAL file

## Slide 101: 6. Write a JAS tester
Such as:
.main
start:
BIPUSH 0x1
MDUP 2
BIPUSH 0x2
MDUP 5
.end-main

## Slide 102: 7. Load/Assemble JAS file
From MMV, load/assemble JAS file
  Choose the tester file
Run the program