## Slide 1: Super Nintendo Entertainment System (SNES) Controller
Jalal Kawash

## Slide 2: Outline
SNES controller

## Slide 3: SNES Controller
Section 1

## Slide 4: Section 1 Objectives At the end of this section you will
Understand the communication protocol of the SNES controller
Write programs to interact with the SNES controller

## Slide 5: GPIO SNES Pins
www.raspberrypi-spy.co.uk
DAT
LAT
CLK

## Slide 6
Ebay.com

## Slide 7: The Controller

## Slide 8: SNES Button Numbers
Button Number/ Clock Cycle | Button
1 | B
2 | Y
3 | Select
4 | Start
5 | Joy-pad UP
6 | Joy-pad DOWN
7 | Joy-pad LEFT
8 | Joy-pad RIGHT
9 | A
10 | X
11 | Left
12 | Right
13-16 | Unused – for future use (always high)
Clock Cycle Button Reported =========== =============== 1 B 2 Y 3 Select 4 Start 5 Up on joypad 6 Down on joypad 7 Left on joypad 8 Right on joypad 9 A 10 X 11 L 12 R 13 none (always high) 14 none (always high) 15 none (always high) 16 none (always high)

## Slide 9: SNES Lines
LATCH: latch line
  Used by the core to instruct the controller to latch the state of the buttons internally
    Which buttons on the controller are pressed
CLOCK: clock line
  The core sends a clock signal of 16 intervals
    One for each button
    Interval 1 is for Button B; 2 for Y etc …
DATA: data line
  Controller sends serial signal to core indicating which buttons are pressed

## Slide 10: Recall GPFSEL{n}
0-2
3-5
6-8
9-11
12-14
15-17
18-20
21-23
24-26
27-29
30-31
reserved
GPIOFSEL{n}
Pin
{n}0
Pin
{n}1
Pin
{n}2
Pin
{n}3
Pin
{n}4
Pin
{n}5
Pin
{n}6
Pin
{n}7
Pin
{n}8
Pin
{n}9

## Slide 11: Initializing SNES – CLOCK line
Set GPIO pin 11 (CLK) to output
#define CLK 11
#define LAT 9
#define DAT 10
INP_GPIO( CLK );

## Slide 12: Initializing SNES
Similarly,
Set GPIO pin 9 (LATCH) to output
Set GPIO pin 10 (DATA) to input (code 0)
INP_GPIO( LAT );
OUT_GPIO( LAT );
INP_GPIO( DAT );

## Slide 13
#define CLK 11
#define LAT 9
#define DAT 10
void initSNES() {
INP_GPIO( CLK ); // CLK
OUT_GPIO( CLK );
INP_GPIO( LAT ); // LATCH
OUT_GPIO( LAT );
INP_GPIO( DAT ); // DATA
}
#define GPIO_BASE 0x3F200000
static unsigned *gpio = (unsigned*)GPIO_BASE; // GPIO base
// GPIO setup macros. Always use INP_GPIO(x) before using OUT_GPIO(x) or SET_GPIO_ALT(x,y)
#define INP_GPIO(g) *(gpio+((g)/10)) &= ~(7<<(((g)%10)*3))
#define OUT_GPIO(g) *(gpio+((g)/10)) |= (1<<(((g)%10)*3))
#define SET_GPIO_ALT(g,a) *(gpio+(((g)/10))) |= (((a)<=3?(a)+4:(a)==4?3:2)<<(((g)%10)*3))

## Slide 14: Communication Protocol
LATCH is used to instruct the SNES to sample and latch buttons
  Which buttons are pressed
  Latched in a register
CLOCK line is used to synchronize serial signal sent from SNES to the core
DATA line is used to read the serialized latched register representing button sampling

## Slide 15: Communication Protocol (1) Core Asks for a report on buttons
Core
SNES
LATCH
LATCH
CLOCK
DATA
CLOCK
DATA
12s

## Slide 16: Communication Protocol (2) SNES Samples Buttons
Sampling buttons = creating a register representation of which buttons are pressed
One bit for each button is sufficient
  Example: 1111101111100
  Three buttons are pressed (buttons 0, 1, & 7)

## Slide 17: Communication Protocol (3) Core pulses clock; SNES to sends report
Core
SNES
LATCH
LATCH
CLOCK
DATA
CLOCK
DATA
12s
6s
B
Y’
Sl
St
’
’
’


## Slide 18: Communication Protocol (3) Core pulses clock; SNES to sends report
Pulsing continues for 16 times
SNES has 12 buttons
  First 12 pulses sample the buttons
Last 4 pulses are not used (always 1)
  Reserved for future extensions

## Slide 19: Communication Protocol (3)
From: homepages.inf.ed.ac.uk

## Slide 20: Reading from SNES
MOV buttons, #0 // register sampling buttons
writeGPIO(CLOCK,#1)
writeGPIO(LATCH,#1)
wait(12s) // signal to SNES to sample buttons
writeGPIO(LATCH,#0)
pulseLoop: // start pulsing to read from SNES
  i = 0
  wait(6s)
  writeGPIO(CLOCK,#0) // falling edge
  wait(6s)
  readGPIO(DATA, b) // read bit i
  buttons[i] = b
  writeGPIO(CLOCK,#1) // rising edge; new cycle
  i++ // next button
  if (i < 16) branch pulseLoop

## Slide 21
16 iterations of pulseLoop
One iteration

## Slide 22: System Timer
Address: 0x3F003004
CHI is the next register, containing the higher 32-bits

## Slide 23: Waiting
#define CLO_REG 0x3F003004
unsigned *clo = (unsigned*)CLO_REG;
unsigned c = *clo + 12; \\ micro Secs
while (c > *clo);