## Slide 1: Video Programming
Jalal Kawash

## Slide 2: Outline
2D arrays
Memory-mapped I/O
Mailboxes
Frame buffer architecture
Drawing basic shapes

## Slide 3: 2D Arrays
Section 1

## Slide 4: Section 1 Objectives At the end of this section you will
Map 2D arrays to 1D arrays
Work with row-major and column-major organizations

## Slide 5: 2D Arrays
Two-dimensional arrays must be mapped onto 1D memory
  Can use row-major ordering
    Store each element of row 0, then row 1, etc.
    Used in most high-level languages, including C, C++
  Or column-major ordering
    Store each element of column 0, then column 1, etc.
    Used by FORTRAN

## Slide 6: Example
Logical arrangement:
10 | 20 | 30
40 | 50 | 60
    Mapping in row-major order:
10 | 20 | 30 | 40 | 50 | 60
10 | 40 | 20 | 50 | 30 | 60
    Mapping in column-major order:

## Slide 7: Indexing 2D Arrays
  The indices for a multidimensional array must be converted into an offset
    Added to array starting address
  For a 2D array list[1..n][1..m], row-major order, list[i][j] is:
        ((m * i) + j)  Esize
      Esize is the element (cell) size in bytes

## Slide 8: Indexing 2D Arrays
Example C Code declaration of
  char array[2][3]
  array[1][2] maps to an offset of
  (3 * 1 + 2) * 1 = 5
0,0 | 0,1 | 0,2
1,0 | 1,1 | 1,2
0 | 1 | 2
3 | 4 | 5
Logical view
Physical view
        ((m * i) + j)  Esize

## Slide 9: Indexing 2D Arrays
Example Java Code declaration of
  char[2][3] array
  array[1][2] maps to an offset of
  (3 * 1 + 2) * 2 = 10
0,0 | 0,1 | 0,2
1,0 | 1,1 | 1,2
0 | 2 | 4
6 | 8 | 10
Logical view
Physical view
        ((m * i) + j)  Esize

## Slide 10: Effective Addresses
A 1D array cell is accessed by:
base + offset
base is the starting address of the array
offset = (cell number) * (cell size in bytes)

## Slide 11: In C
int a[6] = {10, 20, 30, 40, 50, 60};
int *p;
int b;
a[3] = 5; // assign element 3 of a
p = a; // p refers to elements of a
*(p+3) = 5; // does the same assignment
b = a[5]; // assign b value of a[5] – 60
b = *(p+4); // assign b value of a[4] – 50
10 | 20 | 30 | 40 | 50 | 60
a
p

## Slide 12: In C
int a[6] = {10, 20, 30, 40, 50, 60};
int nr = 2, nc = 3; // nr rows, nc columns
int *p;
int b;
a[1 * nc + 2] = 5; // assigns a[1,2]
p = a; // p refers to elements of a
*(p+1*nc+2) = 5; // does the same assignment
b = a[0*nc+2]; // assign b value of a[0,2] – 30
b = *(p+4); // assign b value of a[4] – 50
12
10 | 20 | 30 | 40 | 50 | 60
a
p

## Slide 13: Examples
        myArray: .word 10, 20, 30, 40, 50
Cell containing 10 has address
  myArray + o*4
Cell containing 20 has address
  myArray + 1*4
Cell containing 30 has address
  myArray + 2*4

## Slide 14: Examples
        myArray: .byte 10, 20, 30, 40, 50
Cell containing 10 has address
  myArray + o*1
Cell containing 20 has address
  myArray + 1*1
Cell containing 30 has address
  myArray + 2*1

## Slide 15: Memory-Mapped I/O
Section 2

## Slide 16: Section 2 Objectives At the end of this section you will
Understand memory-mapped I/O
Know how frame-buffers are organized

## Slide 17: Memory-Mapped I/O
A method for performing I/O
Registers and memory of the device are mapped to address values
A Core can communicate with the device by writing and reading memory
  Using loads and stores
To write a register in the I/O device, the core writes to an address in memory
To read a register, the core reads from memory

## Slide 18: Memory-Mapped I/O
Core
RAM
Registers & Memory for I/O device
I/O Device
Bus
DMA

## Slide 19: Memory-Mapped I/O
Easier to program
  I/O does not need special instructions
Takes memory
  Not of a great concern given how cheap RAM is
Not always implemented using DMA
  GPIO registers are not really in memory!

## Slide 20: Frame-Buffers
A frame-buffer is a memory mapped arrangement for monitors
Each pixel is mapped to a memory address
To write a pixel, the core simply sets the corresponding value in main memory
Can be implemented in a separate Video RAM or in a reserved section of RAM
Maps 2D monitor to 1D memory (row-major)

## Slide 21: Frame-Buffer
(GPU) RAM
Video memory
Monitor
pixels

## Slide 22: Memory-mapped I/O
Use ordinary memory instructions to read from or write to the device
Example
      MOV r0, 0x0A0 // address of pixel
      STR r1, [r0] // set pixel
      unsigned *ps = (unsigned*) 0x0A0;
      *ps = color;

## Slide 23: Mailboxes
Section 3
Based on: https://github.com/raspberrypi/firmware/wiki

## Slide 24: Section 3 Objectives At the end of this section you will
Understand the mailbox architecture
Use its registers to read and write
Use the mailbox to initialize a frame buffer

## Slide 25: Mailboxes
Allow communication between the ARM core and the Video Core (VC) in RPi
Mailbox 0 defines 10 channels
  Power management, frame buffer, touch screen etc …
  Frame buffer is channel 1
Mailbox 1 also exists
  Not clear what channels it has

## Slide 26: Mailbox 0 Registers
Register Name | Offset | Purpose
Peek | 0x10 | Read but do not delete info
Read | 0xoo | LS 4 bits = channel number; remaining 28 is data read from mailbox; removes data
Write | 0x20 | Same as read but for writing
Status | 0x18 | Tells if mailbox full or empty
Sender | 0x14 | 
Config | 0x1C | 
Base address for registers is: 0x3F00B880

## Slide 27: Status Register
Bit 31 (MSB) is set when mailbox is full
  Cannot write to mailbox
  Use mask ox80000000 to check it
Bit 30 is set when mailbox is empty
  Cannot read from mailbox
  Use mask 0x40000000

## Slide 28: Read & Write Registers
Bit 0
Bit 1
Bit 2
Bit 3
Bit 4 to 31 = data bits
Channel number

## Slide 29: Reading a Mailbox (for channel n)
Wait until bit 30 in status is clear (=0)
data = read
If data[0..3] != n, goto step 1
(LS 4 bits are the channel number)
Return data[4..31]

## Slide 30
static unsigned *mailbox = (unsigned*)0x2000B880;
#define PEEK 4
#define READ 0
#define WRITE 8
#define STATUS 6
#define SENDER 5
#define CONFIG 7
static unsigned int readMailbox( int channel ) {
unsigned int data;
while ( 1 ) {
// wait until mailbox not empty
while( mailbox[STATUS] & 0x40000000 );
data = mailbox[READ];
if ( (data & 0xf) == channel ) break;
}
return data;
}

## Slide 31: Writing a Mailbox (for channel n)
data[4..31] = value to write
data[0..3] = n
Wait until bit 31 in status is clear (=0)
write = data

## Slide 32
static unsigned *mailbox = (unsigned *)0x2000B880;
#define PEEK 4
#define READ 0
#define WRITE 8
#define STATUS 6
#define SENDER 5
#define CONFIG 7
static void writeMailbox( unsigned int data, int channel ) {
// lowest 4 bits must be zero
if ( data & 0xf ) return;
data |= (channel & 0xf); // put channel no. in 4 lsb
// wait for write status bit to clear
while ( mailbox[STATUS] & 0x80000000 );
mailbox[WRITE] = data;
}

## Slide 33: Mailbox 0 Channels

## Slide 34: Frame Buffer Interface
Send (write) a message via mailbox 0, channel 8 to initialize frame buffer by GPU
The MS 28 bits of message contain the address of a structure (frameBufferInfo) that contains information about the frame buffer
  LS 4 bits contain 8, the channel #
GPU responds with a non-zero message, setting appropriate values in frameBufferInfo

## Slide 35: Initializing the Frame Buffer
Frame
Buffer
Info
FBI
Core
FBI
1000
Mailbox Write Register
GPU
!= 0
1000
Mailbox Read Register

## Slide 36: The frameBufferInfo Array
Created in RAM
Must be 16-byte aligned
  Only the MS 28 bits of the address can be passed through the mailbox
Contains tags
  A tag contains a value buffer

## Slide 37: Tag Structure
Word 1: Tag identifier
  Unique identifier for tag
Word 2: Value buffer size in bytes
Word 3: MSB is request/response bit, remaining bits are value length in bytes
  0 = request; 1 = response
Buffer value

## Slide 38: Example Tag
.int 0x00048003 // Tag ID
//Set Physical Display width and height
.int 8 //size of buffer
.int 8 //length of value
.int 1024 //horizontal resolution
.int 768 //vertical resolution
Tag
Buffer value
MSB = 0 => request

## Slide 39
.align 4
frameBufferInfo:
.int 22 * 4 //Buffer size in bytes
.int 0 //Indicates a request to GPU
.int 0x00048003 //Set Physical Display width and height
.int 8 //size of buffer
.int 8 //length of value
.int 1024 //horizontal resolution
.int 768 //vertical resolution
.int 0x00048004 //Set Virtual Display width and height
.int 8 //size of buffer
.int 8 //length of value
.int 1024 //same as physical display width and height
.int 768
.int 0x00048005 //Set bits per pixel
.int 4 //size of value buffer
.int 4 //length of value
.int 16 //bits per pixel value
.int 0x00040001 //Allocate framebuffer
.int 8 //size of value buffer
.int 8 //length of value
FrameBuffer:
.int 0 //value will be set to framebuffer pointer
.int 0 //value will be set to framebuffer size
.int 0 //end tag, indicates the end of the buffer

## Slide 40: Frame Buffer Interface
1. frameBufferInfo
ARM core
Mailbox 0
Channel 8
GPU (VC)
2. Address of
frameBufferInfo
3. Address of
frameBufferInfo
4. Initialize FB
5. Set FBP, FBS, & pitch
in frameBuffer Info
6. Non-zero message
7. Non-zero message
8. Use FB if FBP !=0

## Slide 41: Frame Buffer Interface (again)
Initialize frameBufferInfo structure
msg[0..3] = 8; msg[4..31] = frameBufferInfo
  msg[30] = 1 (forces GPU to not cache FBI!)
Write msg to mailbox(0)
Read msg from mailbox(0)
If msg == 0, return (FB cannot be initialized)
Else
  FBP = [frameBuffer]
  FBS = [frameBuffer]

## Slide 42: Virtual Frame Buffer
This is only used for debugging the frame buffer subsystem
It is a frame buffer that is created in RAM, rather than VRAM
Writing to the virtual FB will not be visible
  Useful for systems that do not have a graphics display (embedded systems)

## Slide 43: Frame Buffer Architecture
Section 4

## Slide 44: Section 4 Objectives At the end of this section you will
Work with the video frame buffer
Understand color resolutions
Calculate the effective address of a pixel

## Slide 45: Video frame buffer

## Slide 46: Frame Buffer Architecture
Frame buffer:
An array in memory (GPU RAM), where each element represents a pixel on the display
The entire array represents one complete frame (screen)
The 2D frame is mapped to the 1D buffer
  e.g. VGA is 640 x 480
    Maps to a 1D array with 307,200 elements

## Slide 47: Example Resolutions
Standard | Size | Aspect Ratio
VGA | 640 x 480 | 4:3
SVGA | 800 x 600 | 4:3
XGA | 1024 x 768 | 4:3
SXGA | 1280 x 1024 | 5:4
UXGA | 1600 x 1200 | 4:3

## Slide 48: Frame Buffer Architecture
Each element in the frame buffer represents the pixel’s color
  Size in bits per pixel (bpp) Gives 2bbp colors
Row major organization

## Slide 49: Common Graphics Formats
Color depths:
1-bit
  monochrome
4-bit
  16 fixed colors
8-bit indexed
  Choice of 256 colors from a palette
16-bit highcolor
  65,536 colors
  5 bits for R, B; 6 bits for G
24-bit truecolor
  16,777,216 colors
  8 bits each for R, G, and B
32-bit RGBA
  Like truecolor

## Slide 50: Higher Resolution
Higher resolution and/or color depth requires a larger frame buffer
  Practical now since RAM is cheap

## Slide 51: Drawing a Pixel
To draw a single pixel, set its value in the frame buffer
  Must map from 2D logical space to 1D physical RAM
    Must know width and height for particular resolution
  Use formula: element offset = (y * width) + x
    x, y are pixel’s coordinates
    Origin is upper left-hand corner
    x range: 0 to width-1
    y range: 0 to height-1
  physical offset = element offset * element size in bytes

## Slide 52: Alternatively
To draw a single pixel, set its value in the frame buffer
  Must map from 2D logical space to 1D physical RAM
    Must know pitch and element size for particular resolution
  Use formula: row offset = y * pitch
    x, y are pixel’s coordinates
    Origin is upper left-hand corner
    x range: 0 to width-1
    y range: 0 to height-1
    pitch is number of bytes in row
      not necessarily equal to number of elements * size!
  physical offset = row offset + x*element size (bytes)

## Slide 53: Drawing a Pixel
Monitor
Video RAM
pixel

## Slide 54: Drawing a Pixel
Monitor
Video RAM
pixel
0xFF

## Slide 55: Color Codes
Refer to: http://www.nthelp.com/colorcodes.htm

## Slide 56: Frame Buffer Coordinates
x
y
XGA
1024x768
(0,0)
(1023,767)

## Slide 57: Examples
E.g. XGA (1 byte per pixel, 8-bit indexed)
element offset = (y * width) + x
  Pixel (0,0)
    [(0 * 1024) + 0] * 1 = 0
  Pixel (1023, 767) (lower right-hand corner)
    [(767 * 1024) + 1023] * 1 = 786431